## Slide 1: Background- Network Management
Background
Network management (NM) consists of the set of functions to control, plan, allocate, deploy, coordinate, and monitor network resources.
NM architecture begins with the requirements and flow analyses.
Areas addressed during the analysis process include:
  Which network management protocol to apply
  Implementing high-level asset management as part of the network management architecture

## Slide 2: Need -Network Management Architecture
  Reconfiguring the network often to meet various different requirements.
  The need to monitor the entire system from a single location or device.
  Testing service-provider compliance with SLAs and policies.
  The need for proactive monitoring (discovering performance problems before users, applications, and devices are impacted by them).
  Requirements for out-of-band access.

## Slide 3: Defining Network Management
Defining Network Management
NM can be viewed as a top-down approach structure consisting of multiple layers of managements:
  Business Management: budgets/resources, planning, and agreements.
  Service Management: delivery of services to users (for service providers this would include the management of access bandwidth, data storage, and application delivery)
  Network Management: network devices across the entire network.
  Element Management: collection of similar network devices (access routers or subscriber management systems)
  Network-Element Management: individual network devices (a single router, switch, or hub)

## Slide 4: Network Management Hirarchy

## Slide 5: Network Management Defining (cont.)
Defining Network Management
NM can be divided into two basic functions:
  The transport of management information across the system
  The management of NM information elements
Variety of tasks (monitoring, configuring, troubleshooting, and planning)
Define what network management really means to the organizations
There are four categories of network management tasks:
  Monitoring for event notification
  Monitoring for trend analysis and planning
  Configuration of network parameters
  Troubleshooting the network

## Slide 6: Network Management with Elements

## Slide 7: Network Devices and Characteristics
Network Devices and Characteristics
A network device is an individual component of the network that participates at one or more of the protocol layers. (end devices, routers, switches, data service units DSUs, hubs, and NICs)
Network devices have characteristics that can be measured.
They are grouped into:
  End-to-end
  Per-link
  Per-network
  Per-element characteristics

## Slide 8: Network Management – End-to-End Characteristics
End-to-end characteristics:
can be measured across multiple network devices in the path of one or more traffic flows, and may be extended across the entire network or between devices.
  Examples: Availability, Capacity, Delay, Delay variation (jitter), Throughput, Error rates and Network utilization
These characteristics may be modified or added to, depending on the types of traffic on the network.

## Slide 9: Network Devices and Characteristics (cont.)
Network Devices and Characteristics
Per-link/per-network and per-element characteristics :
  Specific to the type of element or connection between elements
  May be used individually, or combined to form an end-to-end characteristic.
  Examples of per-link characteristics:
    Propagation delay
    Link utilization
  Examples of per-element characteristics:
    IP forwarding rates (IP packets/second)
    Buffer utilization for the router
    Logs of authentication failures.

## Slide 10: Measurement of Network
Management of network devices and networks includes:
  Network planning (e.g., cell site planning for wireless)
  Initial resource allocation (e.g., frequency or bandwidth allocations)
  From the telecommunication network management model: FCAPS Fault, Configuration, Accounting, Performance, and Security management.

## Slide 11: Network Management Mechanism
Network Management Mechanisms
Two major network management protocols:
  Simple Network Management Protocol (SNMP)
  Common Management Information Protocol (CMIP).
    CMIP includes CMIP over TCPIP (CMOT).
Management protocols provide mechanism for
  retrieving, changing, and transport of network management data across the network.

## Slide 12: Network Management Mechanism (cont.)
Architectural Considerations
NM process consists of:
  choosing which characteristics to monitor/manage
  Instrumenting network devices to collect necessary data
  Processing data for:
    viewing, storage, and/or reporting;
    displaying a subset of the results
    storing or archiving some subset of the data.
Capturing of other features; using the FCAPS management model:
  Fault management
    processing of events and alarms
    problem identification, isolation, troubleshooting, and resolution;
    returning the network to an operational state.
  Configuration management
    setting system parameters for turn-up
    provisioning the network; configuration and system backups and restores
    developing and operating system databases.
  Accounting management
    monitoring and managing subscriber service usage
    service billing.

## Slide 13: Architectural Consideration
Architectural Considerations
Capturing of other features; using the FCAPS management model :
  Performance management
    implementing performance controls, based on the IP services architecture
    collecting network performance data
    Analyzing performance data
    generating short- and long-term reports from this data
    controlling network and system performance parameters.
  Security management
    implementing security controls
    collecting and analyzing security data
    Generating security reports and logs from this data.

## Slide 14: Architectural Consideration- Network Management
The NM process and management model both provide input to the network management architecture.
Network management needs to consider the following in the architecture:
  In-band and out-of-band management
  Centralized, distributed, and hierarchical management
  Scaling network management traffic
  Checks and balances
  Managing network management data
  MIB selection
  Integration into OSS

## Slide 15: In-Band and Out of Band Network Management
In-Band and Out-of-Band Management
In-band management occurs when the traffic flows for network management follow the same network paths as the traffic flows for users and their applications.
simplifies the network management architecture (Figure 7.8).
Management flows can be impacted by same problems that impact user traffic flows
  If management is most needed, it may not be available
    If management data flows delayed or blocked
  hard to perform event monitoring when
    network under stress (congested)
    network hardware/software configuration problems
    under security attacks

## Slide 16: Traffic Flows for In-Band Management

## Slide 17: Out of Band Network Management
In-Band and Out-of-Band Management
Out-of-band management occurs when different paths are provided for network management data flows and user traffic flows.
allowing the management system to continue to monitor the network during most network events, even when such events disable the network.
Can allow monitoring portions of the network that are unreachable through normal paths (i.e., user data flow paths).
usually provided via a separate network, such as . (Figure 7.9):
  frame relay
  plain old telephone service (POTS) connections.
Having separate network for management:
  additional security features

## Slide 18: Traffic Flows for Out-of-Band Network Management

## Slide 19: In and Out Band Network Management
In-Band and Out-of-Band Management
Out-of-band can be used to troubleshoot and configure remote devices
  saves time and resources when:
    the user data network is down
    No enough human resources
Regular availability checking is needed.
added expense and complexity
to reduce expenses:
  provide out-of-band monitoring at a low level of performance (phone lines)
For some networks a combination of in-band and out-of-band could used, when:
performance of user data network is needed to support network management data flows the expense of a separate network is still incurred.
security issues on the user data network still need to be addressed.
the separate, out-of-band network is needed when the user data network is down.

## Slide 20: Combined In-ban and Out-of-band Management

## Slide 21: Network Management Types
Centralized, Distributed, and Hierarchical Management
Centralized management: all management data (e.g., pings, SNMP polls/responses, Traceroute, etc.) radiate from a single management system (Figure 7.8).
advantage :
  only one management system is needed
  simplifying the architecture and reducing costs
has a variety of management tools associated with it.
Trade-offs:
  single point of failure
  causing congestion or failure on the Network Interface.

## Slide 22: Flow Management for In-Band

## Slide 23: Network Management - Distrubted
Centralized, Distributed, and Hierarchical Management
Distributed : multiple separate components to the management system, placed across the network, localizing network management and distributing management domains. (Fig.7.11)
multiple local element management systems are used to distribute management functions across several domains.
the components either provide:
  all management functions (monitoring, display, storage, and processing)
  the distributed components are the monitoring devices
    Example:
      distributed management may take the form of having multiple management systems on the network (e.g., one management system per campus or per management domain, Figure 7.11)
      single management system with several monitoring nodes, Figure 7.12.

## Slide 24: Distributed Network Management

## Slide 25: Centralized, Distributed, and Hierarchical Management Types
Centralized, Distributed, and Hierarchical Management
    Example:
      distributed management may take the form of having multiple management systems on the network (e.g., one management system per campus or per management domain, Figure 7.11)
      single management system with several monitoring nodes, Figure 7.12.

## Slide 26: Distributed Management

## Slide 27: Hierarchical - Network Management
Centralized, Distributed, and Hierarchical Management
Hierarchical : management functions (monitoring, display, storage, and processing) are separated and placed on separate devices.
separated functions considered as layers communicating in hierarchical fashion. ( Fig.7.13)
localized monitoring devices:
  collect management data
  pass data to display and storage devices
  when data passed on to display and storage devices without processing
    the monitoring devices act as they did in distributed management
    localizing the data collection and reducing the amounts of management data that transit the network.

## Slide 28: Hierarchial with Separate Network Management

## Slide 29: Advantages of Hierarchical Management
Centralized, Distributed, and Hierarchical Management
Hierarchical :
When data are processed before being sent to display and storage devices:
  the monitoring devices act as local filters
  sending only relevant data
  Can reduce amount of management data in the network
Advantages:
  every component can be made redundant
  every component can be independent of the other components
  can be tailored to the specific needs of the network
    several display devices
    several processing devices
    several storage devices
  A trade-off:
    Cost
    Complexity
    Overhead

## Slide 30
References
1. Network Management Systems Architectural Leading Practices, https://www.cisco.com/en/US/technologies/tk869/tk769/technologies_white_paper0900aecd806bfb4c.html
2. Terry Slattery, A Network Management Architecture, https://netcraftsmen.com/a-network-management-architecture-part-1/