## Slide 1: Network Management Fundamentals
Common Management Protocols: Languages of Management
Part I

## Slide 2: SNMP
Simple Network Management Protocol (SNMP)
The original SNMP protocol is today often referred to as SNMP version 1, or simply SNMP-v1
The other protocol was the Common Management Information Protocol (CMIP)
CMIP turned out to be much more complex to implement and, therefore, never gained widespread commercial relevance, validating the design decision to keep SNMP simple.

## Slide 3: SNMP Primitive Operations
Operations | Operated by: | Functionality
Get Request | Manager | Retrieve management information from a MIB
Get-Next Request | Manager | Retrieve management information from a MIB
Set Request | Manager | Write to a MIB
Get-Response | Agent | Respond to get, get-next, and set requests
Trap | Agent | Send event messages

## Slide 4: Get Request
A manager uses a get request to retrieve management information—that is, MIB objects—from an agent.
In addition to an identifier for the request, a get request includes as a parameter a list of variable bindings that specify which objects are requested.
Although more than one MIB object can be retrieved at a time, with SNMP, delivery of messages only up to a certain size (possibly as small as 484 octets, or bytes) is assured.

## Slide 5: Get-Next Request
A manager uses a get-next request to retrieve management information from an agent, just as with a get request.
However, contrary to an ordinary get request, the OIDs in the variable bindings do not specify the objects that are to be retrieved directly.
Instead, for each OID specified in the request, the agent is requested to return the object with the OID that comes in lexicographical order right after that OID.
Example: What is the name of the student sitting next to Jack?

## Slide 6: Get-Next Request (2)
A get-next request directed at countA has the same effect as a get request directed at the object after it, countB.

## Slide 7: Walking a MIB
So why would anyone need an operation like this, when a manager could use a get request and simply specify the desired object’s OID directly?
The reason is that in quite a few situations, the manager actually might not know what objects are in a MIB and hence what OIDs to ask for.
Using get-next requests, a manager can effectively discover an agent’s MIB.
The manager can simply start with an OID of 0 to retrieve the first object, use that object’s OID to retrieve the next one, and so forth.

## Slide 8: Set Request
The first, most obvious, and most common use of set requests is to change the way a device is configured by adjusting certain parameter settings.
A second use is to cause the creation and deletion of logical entities in a MIB.
A third use, stretching the set semantics even further, is to cause the device to perform an action.

## Slide 9: Set Request – Ping Operation

## Slide 10: Set Request – Pinging using MIB

## Slide 11: Get Response
An agent sends a get-response to a manager in response to a request.
Name very confusing; why not call it “Send Response”?
The identifier of the request that it contains the response to.
An error status that amounts to a response code that indicates whether the request was successful or resulted in an error.
An error index that carries further information, in case an error did occur.
A list of variable bindings.

## Slide 12: Get Response Variable Bindings
A list of variable bindings. The variable bindings contain management information that is returned as part of the response.
In case of a response to a get request, each variable binding contains the OID and value of a MIB object that was retrieved.
The same is true in case of a response to a get-next request—note that the OID in the get-response therefore does not correspond to the OID in the variable binding of the get-next request, which contained an OID that lexicographically preceded the retrieved object’s OID.
In the case of a response to a set operation, the variable bindings contain the OIDs of the objects that were set and the values they were set to, basically repeating the information of the set request itself.

## Slide 13: Trap (Event based)
A trap is used to convey an event by an agent to a manager. It is unconfirmed—that is, the manager is not expected to send a response back to the agent.
  Who is emitting the trap—Parameters that specify the address of the agent and the type of system that is emitting the trap.
  What occurred—Parameters that identify the type of event.
  When it occurred—A time stamp of when the trap was generated by the emitting system
Additional information, conveyed in a set of variable bindings—Those variable bindings contain objects with their OIDs and values that could be of interest to the receiving manager.
For example, a trap that indicates that a printer has jammed might include also the location of the printer (if configured in a corresponding MIB object), the identifier of the print job during which the jam occurred, and the user to which the print job belongs. If this information is included with the trap, it saves the manager from needing to issue subsequent get requests. This not only increases management communication efficiency, but it can also improve reaction time.

## Slide 14: SNMP Message Structure
The SNMP version number.
A community string. This string must match a corresponding string that is configured at the device with the SNMP agent for the request to be accepted. In effect, it amounts to a password.
Because this password is not encoded but sent in the clear, and because no other form of authentication of the sender takes place, SNMPv1 is considered to have very weak security—an issue discussed in the next section.
The SNMP protocol data unit (PDU). This is the encoded SNMP operation itself, including a field that identifies the type of operation along with the operation parameters

## Slide 15: SNMP-v1 Issues
No concept of scoping or bulk requests: inefficient at retrieving large amounts of management information.
Offers only minimal security, making it vulnerable to security threats, which effectively prevents SNMPv1 from being used to change the configuration of managed devices—in many cases, the risk of compromising the integrity of the network is simply too great.
Being used mainly for monitoring, but not for provisioning applications, even though it originally was intended as a generic protocol to cover the entire breadth of management functions.
Lack of capabilities such as the creation and deletion of logical entities by management applications in a more straightforward manner.

## Slide 16: SNMP-v2 New Operations
Get-bulk request: what if the manager wants not just the next object, but also the ones after that? The get-bulk request addresses this.
The get-bulk request operation enables managers to retrieve larger chunks of management information with one request.
Inform request: This operation amounts to a notification that the recipient needs to confirm—that is, acknowledge.
Whereas the trap operation allows the sending of notifications unidirectionally (and unreliably), the inform request provides a mechanism that allows an SNMP agent to send reliable events.

## Slide 17: SNMP-v3
Introduces alignments to SNMP messages to carry proper security parameters that finally make SNMP a secure protocol.
  Encryption of management messages
  Strong authentication of senders
  SNMPv3 is much less vulnerable to security attacks
Now for the first time, when an agent receives an SNMP request, it can determine with confidence that an authorized manager issued the request and that the message was not tampered with.

## Slide 18: References
What is SNMP? https://www.thousandeyes.com/learning/techtorials/snmp-simple-network-management-protocol
SNMP Primitives, https://www.pcwdld.com/what-is-snmp-and-tutorial
SNMP protocol overview, https://www.freesoft.org/CIE/Topics/108.htm