## Slide 1: Network Management Fundamentals
Common Management Protocols: Languages of Management
Part II

## Slide 2: Command-line interface (CLI)
Help functions (typing a ? behind a command to display the list of available command options)
  Auto-completion (needing to type only the first few characters of a command or option that make it unique, and using the Tab key to tell the system to fill in the rest)
  Prompts (enabling you to enter different command modes, and reminding you of that mode by the form that the prompt takes)

## Slide 3: “show” Command

## Slide 4: CLI “show” Command Hierarchy

## Slide 5: “show” in Table Format

## Slide 6: syslog Overview
As the name indicates, the purpose of syslog is to write system messages to a log—that is, to a file where a system administrator can analyze them as needed.
Each syslog message is essentially intended to result in an entry in that log.
However, by posing as a logging host, management applications can often receive messages directly as they occur, without needing to take the detour of retrieving log entries from a log file.
syslog is essentially the ideal natural complement to CLI. It provides the capability for the device to emit event messages without solicitation, which complements the request/response pattern of CLI.
syslog is often the only way available to obtain messages about certain events.

## Slide 7: syslog Information

## Slide 8: syslog Message Header & Body
Message body
  Contains the content of the message itself.
  It is the “informal” part of a syslog message
  Not subject to any inherent constraints.
  In many cases, it simply contains plain English text. The
Message header:
  essential information about the message itself
  in a very structured manner.
  the time when the message was emitted
  the name of the host that emitted the message,
  the severity of the message (anything from alert to debug)
  the subsystem that emitted the message (often referred to as facility)
  mnemonic (that is, a name for the type of message).

## Slide 9: IETF syslog Protocol
The priority is a combination of a facility and a severity. The severity is a number from 0 to 7, with 0 being the most severe and 7 being the least severe.
The version number of the syslog protocol.
The time stamp, according to a well-defined format.
The host name, identifying the system from which the syslog message originates.
The application name and the process ID, which identify the subsystem and process that are responsible for emitting the message.
Finally, the message ID, an identifier of the type of syslog message.

## Slide 10: syslog Deployment
However, syslog receivers often have no role in actively managing a device.
In fact, in many cases, the receiver resides in the device itself.
The syslog receiver is simply the receiving end of a syslog message that is generally responsible for logging the message to a file on a disk.

## Slide 11: Circular Log File

## Slide 12: Centralized Logging Host

## Slide 13: syslog Relay

## Slide 14: Netconf: Protocol for a New Generation
It is geared specifically toward managing the configuration of data-networking devices;
Not targeted at monitoring functions and managing state information—SNMP will take care of that;
Netconf allows for the retrieval of state information, although this does not constitute a central capability;
Netconf is best positioned in the configuration management space, where it can fill the void left by SNMP and CLI;

## Slide 15: Netconf Datastores
It is a configuration file, or MIB

## Slide 16: Netconf Architecture

## Slide 17: Netconf Architecture (2)
The transport protocol layer provides for the underlying communication transport.
  Provide support for authentication.
  Upper Netconf layers do not provide this function.
The RPC layer provides primitives that enable managers to invoke functions on agents, using a request-response pattern.
The operations layer contains the management operations themselves.
  Managing the management association itself
  Operations to manipulate and push around configuration files
The content layer deals with the management payload
  Configuration data that is contained in the configuration files

## Slide 18: Netconf Message Structure
Management content in the message is encapsulated by Netconf operations and their parameters, which, in turn, are encapsulated in an RPC wrapper, which, in turn, is put on a transport in the application protocol layer.

## Slide 19: Netconf Operations
get-config is used to retrieve a config file from the device
get is a generalization of get-config. It is the only Netconf operation that goes beyond configuration information and allows the retrieval of state information as well;
edit-config is used to modify and change a configuration—that is, the contents of a configuration datastore.
copy-config is also used to change a configuration. Unlike edit-config, the change is not made within a configuration; the configuration target is replaced in its entirety.

## Slide 20: Netconf Operations (2)
delete-config removes a configuration from a device.
Lock and unlock enable a manager to request exclusive access to a configuration. While a manager holds a lock, other users are not allowed to change the configuration.
Close session is the graceful variant that allows operations that are already in progress to end before the session is torn down
Kill session: aborts the session abruptly

## Slide 21: Netflow Protocol
This protocol simply consists of putting flow records into Netflow packets and exporting those packets to a recipient. The recipient of Netflow packets is commonly referred to as a Netflow collector.

## Slide 22: Netflow Protocol (2)
A header contains bookkeeping information:
  The sequence number of the packet, for storing packets that are received in the proper order and determining whether any data is missing
  The number of flow records contained in the Netflow packet
  The version number of the Netflow protocol itself
The header is followed by a sequence of flow records. Each flow record includes the keys that identify the flow, as well as the statistical data collected for it.

## Slide 23: Management Protocol Positioning