## Slide 1: Network Management System- Concept
The Concept
  From a central computer, network administrator can manage entire network
    Collect data
    Give commands
  Moving gradually toward this ideal

## Slide 2: Network Management System: SNMP
Standards
  Most widely used is the Simple Network Management Protocol (SNMP)
  Other standards exist

## Slide 3: Network Management System: Manager
The Manager
  Software on network administrator's computer
  Short for “network management software”
  Implements network management support

## Slide 4: Network Management System: Managed Nodes
Managed Nodes
  Routers, client PCs, etc. that are managed

## Slide 5: Network Management System: Agents
Agents
  Network management agents
  Installed in managed nodes
  Communicate with the manager on behalf of the node

## Slide 6: Network Management System: RMON
RMON Probes
  Remote MONitoring
  SNMP only
  Special type of agent
  Collects data on a LAN’s traffic: packet sizes, error rates, etc.

## Slide 7: Network Management System: Objects
Objects
  Managed nodes have several objects that are managed
  For instance, on a client PC, one object might be the status of a TCP connection to a particular server
  Another example would be the status of a router port

## Slide 8: Network Management System: Objects (cont.)
Objects
  A managed node may have several “instances” of some objects; For instance, a router may have several ports

## Slide 9: Network Management System: MIB
Management Information Base (MIB)
  Stores collected information
  Schema
    The overall design
    Entities (objects) and attributes
    Object-oriented database
  The actual stored information
  “MIB” is used to refer both to the schema and the actual data
MIB

## Slide 10: Network Management System: MIB (cont.)
Management Information Base (MIB)
  Full MIB is stored on the central administration computer
  Relevant portion of the MIB is also stored by each Agent

## Slide 11: Network Management Protocol (cont.)
Network management protocol standardizes Communication between manager and agent
Defines the schema of the MIB
Most popular is the Internet Engineering’s Simple Network Management Protocol (SNMP)
There are others

## Slide 12: Network Management Protocol: SNMP (cont.)
SNMP Requests and Responses
  Manager sends requests
    Really, commands
    Get: give me data
    Set: change your setting (e.g., turn off Port 1)

## Slide 13: Network Management Protocol: SNMP Req and Resp
SNMP Requests and Responses
  Agent sends back responses
    The information
    Confirmation or reason for rejection

## Slide 14: Network Management Protocol: SNMP Traps
SNMP Traps
  Agent can send a message without a prior manager request
  Message is called a trap in SNMP
  For instance, if the agent senses a problem

## Slide 15: References
What is SNMP? https://www.manageengine.com/network-monitoring/what-is-snmp.html
An Introduction to SNMP protocol, https://www.digitalocean.com/community/tutorials/an-introduction-to-snmp-simple-network-management-protocol
Ronald Vetter, Asynchronous Transfer Mode: An Emerging Network Standard for High-Speed Communications, https://www.sciencedirect.com/topics/computer-science/network-management