## Slide 1: Network Monitoring Tools and Systems

## Slide 2: Network Software Tools
Status monitoring tools
Traffic monitoring tools
Route monitoring tools

## Slide 3: Status Monitoring Tools

## Slide 4: ifConfig
Used to assign/read an address to/of an interface
Option -a is to display all interfaces
Notice two interface loop-back (lo0) and Ethernet (hme0)

## Slide 5: Ping
Most basic tool for internet management
Based on ICMP ECHO_REQUEST message
Available on all TCP/IP stacks
Useful for measuring connectivity
Useful for measuring packet loss
Can do auto-discovery of TCP/IP equipped stations on single segment
  Notes
Example:
% ping 205.152.8.138
PING 205.152.8.138 (205.152.8.138): 56 data bytes
64 bytes from 205.152.8.138: icmp_seq=0 ttl=17 time=14.8 ms
64 bytes from 205.152.8.138: icmp_seq=1 ttl=17 time=20.2 ms
64 bytes from 205.152.8.138: icmp_seq=2 ttl=17 time=15.7 ms
64 bytes from 205.152.8.138: icmp_seq=3 ttl=17 time=21.6 ms
64 bytes from 205.152.8.138: icmp_seq=4 ttl=17 time=20.0 ms
--- 205.152.8.138 ping statistics ---
5 packets transmitted, 5 packets received, 0% packet loss
round-trip min/avg/max = 14.8/18.4/21.6 ms

## Slide 6: nslookup
An interactive program for querying Internet Domain Name System servers
Converts a hostname into an IP address and vice versa querying DNS
Useful to identify the subnet a host or node belongs to
Lists contents of a domain, displaying DNS record
Available with BSD UNIX; FTP from uunet.uu.net
Available in Windows NT
Example:

## Slide 7: Domain Name Groper: dig
Used to gather lots of information on hosts from DNS
Example:
noc2% dig noc2
; <<>> DiG 2.2 <<>> noc2
;; res options: init recurs defnam dnsrch
;; got answer:
;; ->>HEADER<<- opcode: QUERY, status: NXDOMAIN, id: 6
;; flags: qr aa rd ra; Ques: 1, Ans: 0, Auth: 1, Addit: 0
;; QUESTIONS:
;; noc2, type = A, class = IN
;; AUTHORITY RECORDS:
. 86400 SOA A.ROOT-SERVERS.NET. hostmaster.INTERNIC.NET. (
1998091500 ; serial
1800 ; refresh (30 mins)
900 ; retry (15 mins)
604800 ; expire (7 days)
86400 ) ; minimum (1 day)
;; Total query time: 141 msec
;; FROM: noc2.btc.gatech.edu to SERVER: default -- 199.77.147.28
;; WHEN: Wed Sep 16 21:42:11 1998
;; MSG SIZE sent: 22 rcvd: 95

## Slide 8: Host
Command: host
Displays host names using DNS
Available from ftp.nikhef.nl:/pub/network/host.tar.Z
Example:
% host -a sun4-gw.cc.gatech.edu
Trying null domain
rcode = 0 (Success), ancount=1
The following answer is not authoritative:
sun4-gw.cc.gatech.edu 85851 IN A 130.207.111.100

## Slide 9: Traffic Monitoring Tools
  Notes
ping and bing used to measure the propagation characteristics of the transmission path
etherfind, snoop, and tcpdump puts the network interface in promiscuous mode and logs the data

## Slide 10: Packet Loss Measurement
Command: ping
Many options available
Implementation varies from system to system
Example:

## Slide 11: bing
Used to determine throughput of a link
Uses icmp_echo utility
Knowing packet size and delay, calculates bandwidth
bing L1 and L2 and the difference yields the bandwidth of link L1-L2
Bandwidth of link L1-L2 could be higher than the intermediate links.

## Slide 12: snoop
Puts a network interface in promiscuous mode
Logs data on
  Protocol type
  Length
  Source address
  Destination address
  Reading of user data limited to superuser
  Example: Options: -d for device interface and -c for counts

## Slide 13: tcpdump
Command: tcpdump
Interprets and prints headers for:
Ethernet IP ICMP
TCP UDP NFS
ND ARP Appletalk
Useful for examining and evaluating the TCP based traffic
Available in UNIX system; FTP from ftp.ee.lbl.gov
Example: SNMP message

## Slide 14: Network Routing Tools

## Slide 15: Network Status
netstat -a
UDP
Local Address State
-------------------- -------
*.route Idle
*.* Unbound
*.sunrpc Idle
*.* Unbound
*.32771 Idle
*.32773 Idle TCP
TCP
Local Address Remote Address Swind Send-Q Rwind Recv-Q State
-------------------- -------------------- ----- ------ ----- ------ -------
*.* *.* 0 0 0 0 IDLE
*.sunrpc *.* 0 0 0 0 LISTEN
*.39136 *.* 0 0 0 0 IDLE
*.32771 *.* 0 0 0 0 LISTEN
*.32772 *.* 0 0 0 0 LISTEN
*.ftp *.* 0 0 0 0 LISTEN
*.telnet *.* 0 0 0 0 LISTEN

## Slide 16: Route Tracing
Command: traceroute (UNIX) / tracert (MS TIME-EXCEED error report
Available in most UNIX OS
Windows)
ICMP Also available from uc.msc.unm.edu
Discovers route taken by packets from source to destination
Useful for diagnosing route failures
Useful for detecting bottleneck nodes

## Slide 17: Trace Route Sample

## Slide 18: Network Management Tools
SNMP command tools
MIB Walk
snmpsniff
Many tools available on public domain. See http://www.btc.gatech.edu/net/management

## Slide 19: SNMP Command Tools
snmptest
snmpget
snmpgetnext
snmpset
snmptrap
snmpwalk
snmpnetstat
Test tool is an interactive tool to get values of several managed objects, one at a time.
Get, Get-next and Set are the SNMP commands that we learned under SNMP architecture / messages. Execution of these will return an SNMP Response message.
SNMPWalk uses snmpgetnext to trace the entire MIB.
Network status command is used to test the status of network connections of a host.

## Slide 20: SNMP Get Command
% snmpget noc5.btc.gatech.edu public system.sysDescr.0
system.sysDescr.0 = OCTET STRING: "SunOS noc5 5.6 Generic_105181-03 sun4u"
Note that the value 0 at the end of the object id indicates that it is a single valued scalar.

## Slide 21: SNMP Get Next Command
% snmpgetnext noc5.btc.gatech.edu public interfaces.ifTable.ifEntry.ifIndex.1
interfaces.ifTable.ifEntry.ifIndex. 2 = INTEGER: 2

## Slide 22: SNMP Set Command
Command: snmpset host community

## Slide 23: Network Status (cont.)
Command: snmpnetstat host community
Useful for finding status of network connections
% snmpnetstat noc5 public
Active Internet Connections
Proto Recv-Q Send-Q Local Address Foreign Address (state)
tcp 0 0 *.* *.* CLOSED
tcp 0 0 localhost.46626 localhost.3456 ESTABLISHED
tcp 0 0 localhost.46626 localhost.3712 ESTABLISHED
tcp 0 0 localhost.46626 localhost.3968 ESTABLISHED
tcp 0 0 localhost.46626 localhost.4224 ESTABLISHED
tcp 0 0 localhost.3456 localhost.46626 ESTABLISHED
tcp 0 0 localhost.3712 localhost.46626 ESTABLISHED
tcp 0 0 localhost.3968 localhost.46626 ESTABLISHED
tcp 0 0 localhost.4224 localhost.46626 ESTABLISHED
tcp 0 0 noc5.41472 noc5.4480 ESTABLISHED
tcp 0 0 noc5.41472 noc5.4736 ESTABLISHED
tcp 0 0 noc5.4480 noc5.41472 ESTABLISHED
tcp 0 0 noc5.4736 noc5.41472 ESTABLISHED

## Slide 24: SNMP Browser
Command: snmpwalk host community [variable name]
Uses Get Next Command
Presents MIB Tree

## Slide 25: SNMP Sniff
snmpsniff -I interface
A tool in Linux / FreeBSD environment
Puts the interface in promiscuous mode and captures snmp PDUs.
Similar to tcpdump

## Slide 26: Protocol Analyzer
Analyzes data packets on any transmission line including LAN
Measurements made locally or remotely
Probe (data capture device) captures data and transfers to the protocol analyzer (no storage)
Data link between probe and protocol analyzer either dial-up or dedicated link or LAN
Protocol analyzer analyzes data at all protocol levels

## Slide 27: RMON Probe
Network Associates Sniffer
  Stand-alone and Networked
HP NetMetrix / HP OpenView
  Communication between probe and analyzer is using SNMP
Data gathered and stored for an extended period of time and analyzed later
Used for gathering traffic statistics and used for configuration management for performance tuning

## Slide 28: Network Statistics
Protocol Analyzers
RMON Probe / Protocol analyzer
MRTG (Multi router traffic grouper)
Home-grown program using tcpdump

## Slide 29
References
Les Cortell, 2020, Network monitoring status tool, https://www.slac.stanford.edu/xorg/nmtf/nmtf-tools.html
Marc Wilson, Linux Network Monitor Software & Tools for Managing & Monitoring Unix/Linux Systems!, 2020. https://www.pcwdld.com/linux-network-monitor-software-and-tools
Mehedi Hasan, Most Comprehensive List of Linux Monitoring Tools For SysAdmin, 2019, https://www.ubuntupit.com/most-comprehensive-list-of-linux-monitoring-tools-for-sysadmin/