## Slide 1: Wireless Security
Ming Yang

## Slide 2: Objectives
To understand data-oriented wireless and mobile networks and security systems:
  Data-oriented wireless networks
    Wireless LAN (WLAN, 802.11)
    World Interoperability for Microwave Access (WiMAX, 802.16)
    Bluetooth (IEEE 802.15)
  Security in WLAN
    Wired Equivalent Privacy (WEP)
    Wi-Fi Protected Access (WPA, WPA 2 – IEEE 802.11i)
  Summary

## Slide 3: WEP vs. Wired Security
Wired Ethernet (the IEEE 802.3 standard) implements no security mechanism in hardware or software.
However, wired Ethernet networks are inherently “secured” since the access to the medium (wires) which carry the data can be restricted or secured.
On the other hand, in “wireless Ethernet” (the IEEE 802.11 standard) there is no provision to restrict access to the (wireless) media.
Comparison is subjective, it was difficult to answer this question.
Loopholes discovered in WEP have pretty much settled the debate, concluding that WEP fails to achieve its goals.

## Slide 4: WEP vs. TWN Security
Category | Scope | Geographical Range | Roaming Support
WEP | Restricted to last-hop wireless connectivity | Limited | Limited
TWN | went beyond the wireless access network and well into the wired network | Large | Full

## Slide 5: Key Establishment in 802.11
Rely on “pre-shared” keys between the mobile node or station (STA) and the Access Points (APs.)
  So, there is NO key establishment protocol being used.
Problems
  Manual configuration of keys
  -> So, open to manual error.
  -> Can not be expected to choose a “strong” key.
  802.11 allows each STA (and AP) in a Basic Service Set (BSS) to be configured with 4 different keys.
    -> 4 user groups  finer control over reliable STA recognition
  In practice, use the same key across BSSs over the whole Extended Service Set (ESS.)
  -> Makes roaming easier and faster. More susceptible to compromise.

## Slide 6: Anonymity in 802.11
802.11 – “IP”-based networks
For a given IP address, it is very difficult to determine the identity of the subscriber, since
  IP addresses are dynamically assigned using protocols such as DHCP (Dynamic Host Configuration Protocol)
  NAT (Network Address Translation) creates two types of IP addresses (i.e., private IP address and global IP address)
    Private IP address  NAT  Globally valid IP address
NOTE: In TWNs, the routing of a call is done using IMSI/TMSI (directly associated with the subscriber)

## Slide 7: 802.11 Authentication

## Slide 8: Open System Authentication
“Default” Authentication Scheme
Allows any and all station to join the network (no authentication).
AP can enforce the use of “Shared Key Authentication (SKA)

## Slide 9: Open System Authentication

## Slide 10: Shared Key Authentication
Based on “challenge-response” mechanism.
Two groups of STAs
  group 1 : access allowed – shared a secret key with AP
  group 2 : access not allowed

## Slide 11: Pre-Shared Key

## Slide 12: Authentication and Handoffs
This re-authentication delay becomes
even more of a bottleneck for real time applications like voice. Although this is not exactly a security loophole, it is a “drawback” of using the security.

## Slide 13: Problems with 802.11 Authentication
Authentication with shared key.
  No way for the AP to reliably determine the exact identity of STA (only checking a “group” of STAs)
One-way Authentication
  STA can not authenticate Network
  Rouge APs can access virtually everything that the STA sends.
Suffers all drawbacks that WEP suffers.

## Slide 14: Pseudo Authentication
Allows only stations which know the network’s SSID to join the network: poses minimal challenge since the SSID of the network is often transmitted in the clear without encryption.

## Slide 15: MAC Address Filtering
Allows stations with certain MAC addresses to join the network: not a very secure authentication scheme since most wireless access cards used by stations allow the user to change their MAC address via software;

## Slide 16: WEP: Confidentiality in 802.11
WEP Packet
Step 1: Calculate Integrity Check Value (ICV), 4 bytes
  ICV is the same as “Message Integrity Check”
Step 2: Select a “master key”
  From one of the “four pre-shared secret keys”
Step 3: Obtain a “key seed”
- How? Select an IV, Concatenate it with the “master key”
Step 4: Generate cipher-text
  Key seed is fed to an RC4 key generator
  The resulting key stream is XORed with MPDU + ICV (step 1)
Step 5: A 4-byte header is appended to the encrypted packet
  3-byte IV value
  1-byte key-id (specifying one of four pre-shared secret keys being used as the “master key”
MPDU: MAC Protocol Data Unit

## Slide 17: Problems in WEP
Using a “stream cipher in synchronous mode” (RC4) for encrypting data packets
  Requires that “key generators” at the two communicating nodes MUST BE kept “synchronized” (Why? The loss of a single bit of a data stream causes the loss of ALL data following the lost bit!)
  In wireless environment, data loss is widespread.
WEP’s approach: Apply encryption/decryption per packet basis. [Changing the problem: from the “session” level to the “packet” level]
  Require to use unique key for every packet.
WEP key = {IV||master key}, 64 bits
  Per-packet key : simple concatenation of IV (24 bits) and master key (40 bits)
  Master Key: fixed (no change), every packet contains it!
  IV: to be sent in clear text

## Slide 18: Data Integrity in 802.11
To detect data modification
How?
  Calculating ICV (Integrity Check Value) over the received data
  Comparing it with the ICV attached in the message
ICV : CRC-32 (Cyclic Redundancy Check 32 bits)
  Not cryptographically computed -> Weak.

## Slide 19: SHA-1 Hashing Example

## Slide 20: Data Integrity in 802.11
802.11 header is not protected by ICV  redirection attack;
Replay attack;

## Slide 21: WEP Confidentiality Issues
First, the IV size at 24 bits was too short – key space is only 16,777,216;
Second, WEP did not specify how to select an IV for each packet;
Third, WEP did not even make it mandatory to vary the IV on a per-packet basis — this means WEP explicitly allowed reuse of per-packet keys.
Fourth, there was no mechanism to ensure that the IV was unique on a per station basis -- thus making a collision even more likely.
No support for STA to authenticate the network.
Finally, simply concatenating the IV with the pre-shared key to obtain a per-packet key is cryptographically unsecure, making WEP vulnerable to attacks.

## Slide 22: WEP vs WAP vs WPA2

## Slide 23: WEP vs WAP vs WPA2