## Slide 2
Design and Development of Smart TV Protector
Donald Privitera1,2, Hossain Shahriar1
1Department of Information Technology
1Kennesaw State University, USA
2Comprensium, Inc, Marietta, Georgia, USA
dp1@nn1.us, hshahria@kennesaw.edu

## Slide 3
SmartTV’s can cost upwards of US$1000.
A SmartTV contains a computer.
SmartTV’s are deployed in large numbers.
SmartTV’s have a long service life.
Why Does A SmartTV Need To Be Protected?

## Slide 4
SmartTV’s can be hacked or infected with malware.
Firmware patches are rare or non-existent.
No anti-malware solutions exist.
Results: loss of privacy, DDOS, bricking, etcetera.
Why Protect A SmartTV? (continued)

## Slide 5
Digital Video Broadcasting (DVB)
  Cable
  Terrestrial
  Satellite
Hybrid Broadcast Broadband Television (HbbTV)
HDMI (Ethernet network interface integration)
USB
Ethernet and/or WiFi
Bluetooth
Attack Vectors To The Onboard Computer

## Slide 6
A subset of DVB; has mass implications due to broadcast.
Web content mixed with TV content.
Typically, a separate browser renders interactive web content over TV content.
Attacks require web links reach out to a website where exploits are downloaded. This has been shown to be a key part of vulnerabilities.
Key Concern - HbbTV

## Slide 7
All known remote vectors rely on the SmartTV to have access to the Internet in order for an exploit to be realized.
Even physical USB vector sometimes requires an Internet connection to fully realize exploits.
KEY: protect the Internet connection = protect SmartTV.
A Common Denominator

## Slide 8
Concept: A SmartTV Protector

## Slide 9
Vector | Attack Mode | Attack Type | Vulnerability Type | Applicability To STV’s | Risk | Secure Internet Mitigates?
USB Exploits | Local | Physical on site | Malware | Some | Low | SOME
Online- user app download | Local | Trojan | Malware | Most | Medium | ALL
Online- user surfing exploit | Local | Browser 1 exploit | Malware | Most | Medium | ALL
Online- HbbTV user surfing exploit | Local | Browser 2 exploit | Malware | Most | Medium | ALL
HbbTV via DVB-T | Remote | Broadcast | Malware | ALL | High | ALL
HbbTV with WiFi connectivity | Local | Side channel | Confidentialty | ALL | Medium | ALL
HbbTV with any internet connectivity | Remote | Broadcast | Confidentiality | ALL | High | ALL
Fake firmware updates | Remote | Man-in-the-middle | Malware | Some | Medium | SOME

## Slide 10
Low cost
Easy to setup and use
Effective
Reliable
Local device acts as a proxy between STV and Internet
Key Design Requirements

## Slide 11
Router/IDS hybrid
Zed Attack Proxy hybrid
Proxy with a secure browser
VPN with cloud malware filtering
Approaches Considered

## Slide 12
Router/IDS hybrid (HARDWARE INTENSIVE)
Zed Attack Proxy hybrid (HARDWARE INTENSIVE)
Proxy with a secure browser (OVERLY COMPLEX)
VPN with cloud malware filtering (SCALABLE/ELASTIC)
Approach Conclusions

## Slide 13
Router/IDS hybrid (HARDWARE INTENSIVE)
Zed Attack Proxy hybrid (HARDWARE INTENSIVE)
Proxy with a secure browser (OVERLY COMPLEX)
VPN with cloud malware filtering (SCALABLE/ELASTIC)
Approach Recommended

## Slide 14
Thank You For Your Consideration!
Design and Development of Smart TV Protector
Donald Privitera1,2, Hossain Shahriar1
1Department of Information Technology
1Kennesaw State University, USA
2Comprensium, Inc, Marietta, Georgia, USA
dp1@nn1.us, hshahria@kennesaw.edu