## Slide 1: IT 3123 Hardware and Software Concepts
Two’s Complement Binary Fractions, Hexadecimal
Notes: 1:11

## Slide 2: Negative Numbers
We use + and – to represent positive and negative numbers.
With computers, we have only two symbols: 0 and 1

## Slide 3: Signed Magnitude
One possible solution is to use one bit of a binary number to represent the sign.
Consider an 8-bit number: One bit for sign, seven for magnitude 0 represents + 1 represents 
I still have the same number of values (28=256 for eight bits) but I can count only about half as high?
Why?

## Slide 4: A Problem with Signed Magnitude
01111111 = +127
11111111 = 127
But what about: 00000000 and 10000000 ? 00000000 = +0 10000000 = 0
We have two values for zero! Bad.
Arithmetic is different than for unsigned integers.

## Slide 5: Two’s Complement
We will use (about) half the possible values for positive numbers; the rest for negative.
Non-negative numbers:
01111111 +127 01111110 +126 00000001 + 1 00000000 0 (and there’s only one!)
Even better, addition, subtraction, and multiplication are the same as for unsigned numbers.

## Slide 6: Interpreting Two’s Complement
The leftmost bit (sign bit) represents a negative number times the power of two indicated by the position.
The remaining bits represent positive numbers added back to the negative value.
ai2i
i=0
n2

−an12n1 

## Slide 7: Negative Numbers
11111111  1 Huh? What? 11111110  2 10000010  126 10000001  127 10000000  128
01111111 +127 01111110 +126 00000010 + 2 00000001 + 1 00000000 0
Positive numbers

## Slide 8: Interpreting Two’s Complement
10000000  128 + 0 = 128 10000001  128 + 1 = 127 10000010  128 + 2 = 126 10000011  128 + 3 = 125
11111111  128 + 127 = 1
1111111 = 271= 64+32+16+8+4+2+1 = 127
Notes: The slide shows some values of two’s complements numbers. There’s my minus 128. It’s a minus 127 plus zero. Minus 127 is minus 128 plus one. Minus 126 is minus 128 plus two. Minus 125 is a minus 128 plus three. … All the way down to minus 128 plus 127 gives me a minus one.

## Slide 9: Two’s Complement Problem
01111111 +127 00000001 + 1 00000000 0 11111111  1 10000000 128
Largest positive number: 127 Largest negative number: 128
There is one more negative number than there are positive numbers. Why?

## Slide 10: Why ?
Every binary number has 2n possible values.
n is the number of bits, and so must be > 0
2n is even for n > 0 (2, 4, 8, 16, 32, etc.)
We use one value for zero.
We now have an odd number of values to split between the positive and negative integers. One half or the other must have one less.

## Slide 11: Asymmetric About Zero
For eight-bit integers… Largest positive number: 127 Largest negative number: 128
There is one more negative number than there are positive numbers.
We say that two’s complement representation is asymmetric about zero.

## Slide 12: Complementing a Number
“Complementing” a number has the effect of multiplying by 1
Two steps:
  Complement (flip) each bit
  Add one to the result.
This is effectively subtracting the number to be complemented from zero.
The “trick” is that we subtract from minus one (all ones) then add one.

## Slide 13: Subtracting from Minus 1
1 1 1 1 1 1 1 1
 0 0 0 1 0 1 1 1 Subtraction from minus 1
1 1 1 0 1 0 0 0
1 1 1 0 1 0 0 0 Complementing each bit
They produce the same result!

## Slide 14: Finding the Two’s Complement
0 0 0 1 0 1 1 1 2 = 2310
1 1 1 0 1 0 0 0 Complement each bit + 1 Add 1 1 1 1 0 1 0 0 1 =  2310

## Slide 15: Did That Work?
1 1 1 0 1 0 0 1  2310 + 0 0 0 1 0 1 1 1 + 2310

## Slide 16: Yes, It Worked!
1 1 1 0 1 0 0 1  2310 + 0 0 0 1 0 1 1 1 + 2310
1 0 0 0 0 0 0 0 0
The carry on the left is discarded because we are working with finite precision arithmetic, in this case, eight bits. So,  23 + 23 = 0 (as expected)
X
Notes: We're doing finite precision arithmetic on eight bits. Our only choice is to discard that ninth bit.

## Slide 17: Complementation Works Both Ways
1 1 1 0 1 0 0 1 2 =  2310
0 0 0 1 0 1 1 0 Complement each bit + 1 Add 1 0 0 0 1 0 1 1 1 = + 2310

## Slide 18: A Shortcut
Copy the bits of the number, from the right, until you have copied a 1 bit.
Invert the remaining bits.
As taught by Dr. Hung and explained to me by someone who had taken the class.
0 0 0 1 0 1 1 1 1 1 1 0 1 0 0 1
1 1 1 0 1 0 0 0 + 1
1 1 1 0 1 0 0 1
0 0 0 1 1 0 1 0
1 1 1 0 0 1 1 0
1 1 1 0 0 1 0 1
+ 1 11 1 0 0 1 1 0
Notes: This works because adding one to a binary number is accomplished by flipping all 1s to 0s from the right until a 0 is reached, flip that to 1 and stop (essentially carrying the overflow of adding 1 to 1).
So one method flips only the bits to the left of the first one, while the other flips all bits, then flips the first 1 (now 0) and the bits to the right of it back.

## Slide 19: Two’s Complement Addition
Use the ordinary rules of binary addition
Any carry out of the leftmost bit is discarded. (But a “flag” is set.)
Notes: The "carry flag" allows operations on large binary numbers to be built up from operations on smaller numbers.)

## Slide 20: Overflow

## Slide 21: The Overflow Rule
If two numbers of opposite signs are added, overflow cannot occur.
If two numbers of the same sign are added, overflow has occurred if and only if the result is of the opposite sign.
Notes: If you add two numbers of opposite sign, the magnitude of the result must be less than either of the addends, so overflow cannot occur.
If you add two numbers of the same sign and get a result that is of the opposite sign, something is wrong! That “something” is that overflow has occurred.
In digital logic, The overflow condition is checked by comparing the carry in to the leftmost bit with the carry out from the leftmost bit. Recall that an XOR gate produces a one, or true, when the input bits are equal and a zero, or false when they’re different. There are two ways that can happen.
Case 1: If the carry in to the leftmost bit is zero, the only way the carry out can be one is if both A and B of the leftmost bit were one, i.e. both negative. The sum of 1+1 (plus zero for the carry in) will be zero with a carry out. The two operands were negative, but the leftmost bit of the result will be zero, or be positive, and overflow has occurred.
Case 2: If the carry in to the leftmost bit is one, the only way carry out can be zero is if both A and B of the leftmost bit were zero, i.e. positive. The sum of 0+0+1 will be one. The two operands were positive, but the carry out will be zero and leftmost bit of the result will be one, or negative, and overflow has occurred.

## Slide 22: Subtraction
Addition is commutative: 5+3 = 3+5
Subtraction is not: 5  3  3  5
The first number, the number being diminished, is called the minuend
The second number is the subtrahend 51 minuend  22 subtrahend 29 difference

## Slide 23: Subtraction Rule
Form the two’s complement of the subtrahend.
Add it to the minuend
We do not need to build special circuits in computers for subtraction; all we need is complementation and addition.

## Slide 24: Sign Extension
Consider this eight-bit number: 0 0 0 1 0 1 1 1
Clearly 00010111 = 0000000000010111
We can store an eight-bit positive number in a 16-bit word by adding zeros on the left.

## Slide 25: Sign Extension
Consider this signed eight-bit number: 1 1 1 0 1 0 0 1
It turns out that: 11101001 = 1111111111101001
The negative multiplier becomes larger 215 instead of 27 but the difference is exactly offset by the additional 1’s added back.

## Slide 26: Sign Extension Rule
Store a twos complement number in a larger space by extending the sign on the left.

## Slide 27: Inspecting Binary Numbers
For two’s complement binary numbers, the leftmost bit tells whether the number is positive or negative.
  0 means positive 1 means negative
For unsigned and two’s complement binary numbers, the rightmost bit tells whether the number is odd or even 0 means even 1 means odd

## Slide 28: Limitations of Two’s Complement
Only integers (whole numbers)
So, no numbers smaller than one but greater than zero
Cannot store really big numbers with 32 bits, the limit is about  two billion

## Slide 29: Summary of Two’s Complement
Positive and negative integers.
Asymmetric about zero
Forming the two’s complement (How?)
Overflow rule (What is it?)
Subtraction rule
Sign-extension rule
Leftmost bit is the sign bit (1 is negative)
Rightmost bit indicates even/odd (1 is odd)

## Slide 30: Decimal Fractions
We use a “decimal point” to represent fractions. 0.1 = 1/10 = 10-1 0.01 = 1/100 = 10-2
Decimal fractions are based on negative powers of 10
Unlike integers, not all fractions can be represented, e.g. 1/3
But we can be arbitrarily precise: 0.3 or 0.33 or 0.3333, or 0.3333333333333, within the limits of finite precision arithmetic.

## Slide 31: Binary Fractions
We use a “binary point” to represent fractions. 0.12 = 1/2 = 2–1 0.012 = 1/4 = 2–2
Binary fractions are based on negative powers of 2
Not all fractions can be represented exactly e.g. 1/3 and 1/10

## Slide 32: Hexadecimal Numbers
Base 16
We need 16 symbols: 0..9, A, B, C, D, E, F Case insensitive.
A represents 1010, B=11, C=12, D=13, E=14, F=15
Positions are powers of 16: 1 16 256 4096 65,536 etc.

## Slide 33: Hexadecimal as Shorthand
Hexadecimal numbers make a convenient shorthand for binary.
How high can we count in four bits?

## Slide 34: Hexadecimal as Shorthand
Hexadecimal numbers make a convenient shorthand for binary.
How high can we count in four bits?
OK… how high can we count with one hexadecimal digit?
15

## Slide 35: Hexadecimal as Shorthand
Hexadecimal numbers make a convenient shorthand for binary.
How high can we count in four bits?
OK… how high can we count with one hexadecimal digit?
One hex digit is exactly equivalent to four binary bits.
15
15

## Slide 36: Hexadecimal as Shorthand
0000 0 1000 8 0001 1 1001 9 0010 2 1010 A 0011 3 1011 B 0100 4 1100 C 0101 5 1101 D 0110 6 1110 E 0111 7 1111 F
Binary Hex
Binary Hex
Hexadecimal numbers are case-insensitive.

## Slide 37: Translating
Hexadecimal to binary: just write down four bits per hex digit 1 716 0001 0111
Binary to hex: mark bits in groups of four from the right; write one hex digit for each four bits 1 0111 1 716

## Slide 38: Translating
Hexadecimal to binary: write down four bits per hex digit A F 2 316 1010 1111 0010 0011
Binary to hex: mark bits in groups of four from the right; write one hex digit for each four bits 1010100101101011
A 9 6 B