## Slide 1: IT 3123 Hardware and Software Concepts
Computer and Memory Organization
Notice: This session is being recorded.

## Slide 2: Announcements
Midterm grades posted.
About grades…
You can see a semester cumulative grade in D2L. (It’s called “final grade.)
Reduced office hours on March 13.
Assignment 3
Minor syllabus revisions.

## Slide 3: The Datapath Computes PC ← PC+1
Incr
Ena A
Write
Control
Notes: In reality, each register has two outputs, A and B, and two Enable lines, Enable-A and Enable-B

## Slide 4: Branch Instructions: BRP
Fetch
Decode
Execute
MAR ← PC (read memory)
Determine next operation
IFP; PC ← IR[addr]
PC ← PC+1
IR ← MDR
IFP tests the P (positive) flag; the branch is only taken if P is true. Branch on zero is similar. Unconditional branch omits the test.
Notes: Natural language description and RTL

## Slide 5: Instructions
Direction given to a computer
Cause electrical signals to be sent through specific circuits for processing
Instruction Set: The collection of instructions a given computer can perform. (TBC has nine instructions; the list of them is its instruction set.)

## Slide 6: Instruction Set
Design defines functions performed by the processor
Differentiates computer architecture by the
  Number of instructions
  Complexity of operations performed by individual instructions
  Data types supported
  Format (layout, fixed vs. variable length)
  Use of registers
  Addressing (size, modes)

## Slide 7: Elements of an Instruction
Operation Code (op-code): Commands the control unit and the ALU what to do
Operands: tell the location of the data to be used in the instruction.
  Source operand: where to get the data
  Result operand: where to put the result (Also called the destination operand.)
The operands are (usually) addresses.

## Slide 8: Operand Addresses
Addresses may be explicit or implicit
Explicit: encoded in the instruction. (The TBC memory address is explicit.)
Implicit: implied by the nature of the operand. (The TBC uses the accumulator implicitly.)
Addresses may refer to memory or to registers.
Operation code 3 25 Operand

## Slide 9: General Form of an Instruction
Op-Code
Source
Operand
Result
Operand
Op-Code
Register Operand
Memory
Operand
A More Specific Form
8 bits
4 bits
20 bits

## Slide 10: Instruction Format
Specific to a particular family of computers (architecture).
Specifies the length of the op-code.
And the size and number of operand fields.
A single computer may have several different instruction formats.

## Slide 11: Categories of Instructions
Data transfer instructions
Arithmetic instructions
Logical operations
Program control
Stack manipulation
I-O and machine control
Multiple-data instructions
Notes: Seven categories

## Slide 12: Data Transfer Instructions
Move data between registers in CPU
Transfer data from memory to a CPU register (load)
Transfer data from a CPU register to memory (store)
Size of a single transfer: generally, the size of a data register; a “word”
Words are 8, 16, 32, 64, or 128 bits
64-bit words are currently most common

## Slide 13: Arithmetic Instructions
The usual suspects: + – / *
Separate instructions for integer and floating-point operands.
Shift and rotate instructions
  One bit shift left multiplies by two
  One bit shift right divides by two
Rotate: Bits shifted out one end are used for replacement bits at the other end.
Increment, complement, etc.

## Slide 14: Logical Operations
Logical AND and OR of two operands
Sometimes others: XOR, NOR, NOT
Relational operations: > < =
Testing for zero, positive, negative

## Slide 15: Program Control
Branch instructions; conditional and unconditional
Call instructions (save program counter someplace)

## Slide 16: Subroutine Linkage Problem
Notes: Calling methods (subroutines or subprograms) we have the same problem as Hansel und Gretel; getting there is no problem, but how to get back?

## Slide 17: Subroutine Linkage Solution
Dynamic allocation of data…
… so that multiple return addresses can be saved.
Data structure: last-in, first-out, so that retrieving an address gets that of the most recent subprogram call.
In computer terms, that’s a stack.

## Slide 18: Stack Manipulation
Many architectures have special instructions for dealing with LIFO data structures (stacks)
push and pop; also call and return

## Slide 19: I-O and Machine Control
Transfers from registers to I-O devices
Direct memory access (DMA) I-O The I-O device communicates with memory independent of the CPU
Machine state switching (privileged instructions)
Interrupt control
State saving
Halt

## Slide 20: Multiple-Data Instructions
Perform the same operation on multiple data items simultaneously (Example: Intel MMX)
Commonly used in vector and array processing
SIMD: Single-instruction, multiple data

## Slide 21: Multiple Data Instructions

## Slide 22: Memory Capacity
Limited by two factors
  Size of the MAR: k bits address 2k cells
  Size of the effective address portion of an instruction. (in LMC, it is two digits, in TLC, eight bits.)
The amount of physical memory is important for performance
Notes: “Effective address” is the address after all address arithmetic.

## Slide 23: Operation of Memory

## Slide 24: Decoders for Large Memories
A 32-bit MAR would need a 32 to four billion decoder; not really practical.
If the address is divided into 16 bits of “row address” and 16 bits of “column address,” each is 216 = 65,536 lines.
Decoding is necessarily slower for very large memories.
Decoding happens within the memory chips, not in the CPU. That keeps the size of the memory address bus reasonable.

## Slide 25: Volatile and Non-Volatile Memories
Volatile memories lose their contents when power is removed.
Non-volatile memories retain their contents even when powered off.

## Slide 26: Random Access Memory (RAM)
Called “random access” because any cell may be addressed as fast as any other.
Dynamic RAM (DRAM)
  Loses contents when power removed (volatile).
  Must be refreshed thousands of times per second..
Static RAM (SRAM)
  More expensive, faster, no refresh needed.
  Loses contents when power removed(volatile).
SDRAM: Synchronous dynamic RAM.
Notes: SDRAM uses a clock to synchronize the operation of the memory.

## Slide 27: Flash Memory
Non-volatile semiconductor memory
Faster than magnetic disks but more expensive
Uses
  BIOS: initial boot instructions and diagnostics
  Solid-state drives
  Digital cameras, music players, thumb drives, etc.
Slower than RAM
Limited, but fairly large, number of write cycles.

## Slide 28: Read Only Memory (ROM)
Non-volatile memory to hold software that is not expected to change over the life of the system
ROM: Contents fixed when manufactured; cannot be changed.
EEPROM
  Electrically Erasable Programmable ROM
  Slower and less flexible than flash memory
  Used when changes are infrequent

## Slide 29: CMOS Memory
CMOS: Very low power read-write memory; clock and configuration info.
CMOS: Complementary metal-oxide semiconductor.

## Slide 30: Boundary Alignment
Modern computers are byte-addressable, i.e. a program can request any byte.
Transfers between CPU and memory are in words. For a 64-bit CPU, that’s eight bytes.
Data items more than one byte and less than one word should be word-aligned so that only one transfer is needed.
Compilers do this automatically.

## Slide 31: Byte Ordering
The most significant byte of a word can be stored:
  At the lowest address or
  At the highest address.
This is a choice made when the architecture is designed.
  Lowest address called : Big-endian
  Highest address called: Little-endian
Important for data exchange.
Notes: The terms big endian and little endian come from Jonathan Swift’s Gulliver’s Travels, and refer to the
war over which end of an egg to open. They were applied to computer byte ordering by D. Cohen (1981).

## Slide 32: Error Detection: Parity
To each byte, add one extra bit, called a parity bit.
Each time the byte is stored, set the extra bit such that the number of one-bits is even. (Even parity.)
Each time a byte is read, check the number of one bits is still even. If not, a memory error has occurred.
Could use odd parity as well.
Notes: A parity system can detect only errors in an odd number of bits. If two bits are changed erroneously, the parity will be correct even though the contents have been corrupted. Often this is called “detecting single-bit errors.”

## Slide 33: Error-Correcting Codes
Hamming code: adds extra parity bits.
Can detect double-bit errors and correct single- bit errors.
Example: d0 is checked by p0 and p1. If both are in error, then the error must be in d0.
There are other error-correcting codes.
Notes: In 1950, Richard Hamming of Bell Laboratories devised a system to detect multi-bit errors and correct single bit errors, now called
a Hamming code. The principle of the Hamming code is that every data bit is checked by more than one parity bit.
The figure shows four data bits being checked be three parity bits. If data bit d0 were corrupted, parity bits p0 and p1 would both indicate errors. The only data bit checked by both p0 and p1 is d0. If we know which single bit is incorrect, it can be corrected by complementing it, i.e. flipping it back to the other possible value. A fourth parity bit, p3, checks the parity of all the other parity and data bits. A Hamming code like this can correct single-bit errors and detect double-bit errors. The example uses four parity bits to check four data bits, an overhead of 100%. However, the overhead diminishes as the number of data bits to be checked by a Hamming code increases. A 32-bit word can be checked with seven parity bits, six of which check individual data bits and one of which checks the overall
parity.

## Slide 34: Buses
The physical connection that makes it possible to transfer data from one location in the computer system to another
Group of electrical conductors for carrying signals from one location to another
Line: each conductor in the bus

## Slide 35: Bus Signals
3 kinds of signals and sometimes power, which is not a “signal”
  Data (binary numbers: alphanumeric, numerical, instructions)
  Addresses
  Control signals
  Power and ground (sometimes)

## Slide 36: Bus Applications
Connect CPU and Memory
I/O peripherals: on same bus as CPU/memory or separate bus
Physical packaging commonly called backplane or motherboard
  Also called system bus or external bus
  Example of broadcast bus
  Part of printed circuit board called motherboard that holds CPU and related components

## Slide 37: Bus Hierarchy
Processor bus: on-chip
Memory bus (northbridge) Connects the memory subsystem and processor
I/O bus (southbridge)
  Connects I/O to the CPU and memory
  Connects all peripheral cards and connectors
  Examples: SATA, Thunderbolt, and USB

## Slide 38: Motherboard

## Slide 39: Bus Characteristics
Protocol
  Documented agreement for communication
  Specification that spells out the meaning of each line and each signal on each line
Throughput, i.e., data transfer rate in bits per second
Data width in bits carried simultaneously

## Slide 40: Parallel Buses
High throughput because all bits of a word are transmitted simultaneously.
Expensive and require physical space
Subject to electrical interference, which limits their speed and length.
“Bus skew” is the condition that bits on some of the lines arrive before bits on other lines.
If bus skew exceeds one bit time, data are corrupted!
Generally used for short distances such as CPU buses and on computer motherboards.

## Slide 41: Serial Buses
One bit transmitted at a time; so, no skew
Single data line pair and a few control lines.
For many applications, throughput is higher than for parallel because of the lack of electrical interference and absence of skew.
Consider USB (Universal Serial Bus) and SATA (Serial ATA disk attachment).

## Slide 42: PCI Express (PCIe)
A serial/parallel computer expansion (internal) bus
Full duplex operation over two simplex paths, one each direction.
Each pair is a “lane.”
A “link” may be one to 32 lanes.
Lanes transmit byte streams
https://en.wikipedia.org/wiki/PCI_Express

## Slide 43: Point to Point vs. Multipoint
cv
CPU
PCIe Root Complex
Point-to-point
Computer
Computer
Printer
Multipoint

## Slide 44: Bus Organization in Modern CPU

## Slide 45: Virtual Memory
What if a program (or collection of programs) needs more memory than the computer has?
Solution: use disk as a substitute for memory
Managed by the operating system
Built into the hardware
Independent of application (transparent)

## Slide 46: Memory Speed
Memory is slow compared to CPU processing speeds!
  2Ghz CPU = 1 cycle in ½ of a billionth of a second
  20ns DRAM = 1 access in 20 billionths of a second (40 times slower!)

## Slide 47: Memory Enhancements
Methods to improve memory accesses
  Wide Path Memory Access
    Retrieve multiple bytes instead of one byte at a time
  Memory Interleaving
    Partition memory into subsections, each with its own address register and data register
  Cache Memory

## Slide 48: Memory Interleaving

## Slide 49: Cache Memory
A small, fast memory placed between the CPU and main memory
  Blocks: 8 or 16 bytes ; Unit of transfer between storage and cache memory. (Also called a cache line.)
Tags: point to a location in main memory

## Slide 50: Cache Memory
Hit Ratio: ratio of hits out of total requests
  Hit ratios of 90% are common.
Problem: synchronizing cache and memory
  Write through
  Write back

## Slide 51: Step-by-Step Use of Cache: Hit

## Slide 52: Step-by-Step Use of Cache: Miss

## Slide 53: Performance Advantages
Hit ratios of 90% common
50%+ improved execution speed
Locality of reference is why caching works
  Most memory references confined to small region of memory at any given time
  Well-written program in small loop, procedure or function
  Data likely in array
  Variables stored together

## Slide 54: Multi-level Caches

## Slide 55: Cache vs. Virtual Memory
Cache speeds up memory access
Virtual memory increases amount of perceived storage
  independence from the configuration and capacity of the memory system
  low cost per bit

## Slide 56: Questions