## Slide 1: Cyber Physical Systems: Security and Safety
Singapore University of Technology and Design
Aditya P Mathur
December 15, 2012
Adopted from: Aditya P Mathur
International Workshop on Information Security (IWIS-2012)
Notes: http://www.istockphoto.com/stock-illustration-17912107-game-world.php?st=d56805a (temperature 1100K)

## Slide 2: Questions of interest
What is a CPS?
What are the security issues in CPS and how do they differ from those in traditional information systems?
To what extent can a CPS be secured against cyber crime?
Are there some fundamental design principles that ought to be used when designing or upgrading a CPS?
What are the curricular ramifications of CPS security?

## Slide 3: Coverage
CPS examples and concerns, components, abstraction, incidents
Traditional versus CPS security
Industrial control systems
Two real-life incidents: Toys and Iran
Control systems: basics
Case studies: Medical devices and Irrigation Systems
CPS: design principles, research and educational needs

## Slide 4: Cyber Physical Systems: Examples

## Slide 5: Shipping
Several countries and cities in the world have some of the world's busiest ports and large transshipment hubs.
For example, PSA Singapore Terminals are connected by 200 shipping lines to 600 ports in 123 countries, with daily sailings to every major port of call in the world.

## Slide 6: Healthcare
Singapore offers Asia's best healthcare system, and its standard of medical practice ranks among the best in the world.
The Joint Commission International (JCI) has accredited 11 hospitals and three medical centers in Singapore.

## Slide 7: Infocomm
Singapore today ranks as the second most network-ready country in the world and the first in Asia, according to the World Economic Forum's Global Information Technology Report 2010/2011.

## Slide 8: Energy
“Today, Singapore is the undisputed oil hub in Asia and is one of the world’s top three export refining centers....”

## Slide 9: Smart Grid - Overview

## Slide 10: Smart Grid – Smart Metering

## Slide 11: Smart Metering Privacy Issue (1)

## Slide 12: Smart Metering Privacy Issue (2)

## Slide 13: Privacy is not Secrecy

## Slide 14: Privacy versus Secrecy

## Slide 15: Possible Solutions
Robust Smart Metering Design with privacy constraints
Utility-Privacy Tradeoff Design
Privacy Invasion Detection/Prevention
Data masking
Data Anonymisation

## Slide 16: Other Potential Concerns:

## Slide 17: CPS Vulnerability
Are your energy, healthcare, water, shipping, transportation systems vulnerable to network attacks?
What, if any, are the vulnerabilities in such systems?
When exploited, how might such vulnerabilities affect people?

## Slide 18: CPS Control systems
Are the control systems in your large and critical CPSs systems robust enough to withstand deception attacks?
Are these control systems programmed to withstand denial of service attacks?

## Slide 19: Surviving from Physical attacks
What happens if we lose part, or even most of the computing systems?
Will redundancy alone solve the problem?
How to measure and quantify of resilience of current systems?
How to ensure high availability of CPS?

## Slide 20: Defending Against Device Capture Attack
Physical devices in CPS systems may be captured, compromised and released back by adversaries.
How to identify and ameliorate the system damage with trusted hardware but potentially untrusted/modified software?

## Slide 21: Real-Time Security in CPS
CPS often requires real-time responses to physical processes
Little Study on how attacks affect the real-time properties of CPS
How to guarantee real-time requirements under attack?

## Slide 22: Concurrency in CPS
CPS is concurrent in nature, running both cyber and physical processes
Little research on handling large-scale concurrent systems

## Slide 23: Collaboration and Isolation
CPS needs to effectively isolate attackers while maintaining collaborations among different, distributed system components
How to avoid cascading failures while minimizing system performance degradation?

## Slide 24: Cyber Physical System: Components

## Slide 25: CPS: Greenhouse

## Slide 26: CPS: Blending process

## Slide 27: CPS Other examples
Pacemaker
ICD (Implantable Cardiovascular Defibrillator)
Insulin pump
Neuro-stimulators

## Slide 28: Cyber Physical Systems: Abstraction

## Slide 29: CPS: Component view

## Slide 30: CPS: Systems View
Physical System
Sensor
Control System
Actuator
y
u: input
x: state
Estimation and control
: Network

## Slide 31: CPS Network-based Attacks
Physical System
Sensor
Control System
Actuator
y’ not y:
Sensor
compromised
u’ not u
controller
compromised
Network
jammed

## Slide 32: Existing Techniques
Authentication
Digital signatures
Access control
Intrusion detection

## Slide 33: Enhancement of existing approaches
How deception and DoS attacks affect application layer performance (e.g., estimation and control)?
Intrusion detection and deception attacks in control systems?
What if a human is not in the loop for intrusion detection?

## Slide 34: CPS incident statistics

## Slide 35: CPS incident databases
BCIT Industry security incident databaseTOFINO http://www.tofinosecurity.com/
Cyber incidents involving control systems, Robert Turk, October 2005, Idaho National Laboratory, INL/EXT-05-00671
Wurldtech: http://www.wurldtech.com/
http://www.tofinosecurity.com/blog/2012-scada-security-predictions-how-did-eric-byres-do

## Slide 36: Sample CPS incidents
2010: Stuxnet [http://www.tofinosecurity.com/stuxnet-central]
Nov 2012: kAndyKAn3 worm attacks North Pole Toys
Over 500 SCADA vulnerabilities found in 2011
2010: Night Dragon, Duqu, Nitro

## Slide 37: CPS incident report statistics
Empirical Analysis of publicly disclosed ICS vulnerabilities since 2001” by Sean McBride

## Slide 38: CPS incident (more) statistics
42% of all incidences were conducted by means of mobile malware
61% of the perpetrators originated from external sources
43% of perpetrators were malware authors

## Slide 39: Traditional versus CPS security

## Slide 40: Traditional
Confidentiality: Ability to maintain secrecy from unauthorized users.
Integrity: Trustworthiness of data received; lack of this leads to deception.
Availability: Ability of the system being accessible

## Slide 41: CPS
Timeliness: responsiveness, freshness of data
Ref: A Taxonomy of Cyber Attacks on SCADA Systems, Zhu et al., UC Berkeley.
Availability: unexpected outages
Integrity: genuine data displayed and received by the controller
Confidentiality: Information regarding SCADA not available to any unauthorized individual
Graceful degradation

## Slide 42: Industrial Control Systems

## Slide 43: SCADA
Supervisory Control and Data Acquisition System
It is an industrial control system that consists of RTUs, PLCs, and HMIs to control an industrial process.
Use: Manufacturing, power generation, fabrication, oil and gas pipelines, etc.

## Slide 44: RTU
Microprocessor controlled Remote Terminal/Telemetry Unit
Interface between physical objects and a SCADA.
Transmits telemetry data to SCADA. Example: water quality.
Siemens LC150 Pump Control Telemetry Unit

## Slide 45: PLC
Programmable Logic Controller
A computer to control the operation of electro-mechanical devices such as pumps, motors, switches
Hard real-time system
Programs stored in non-volatile memory, battery backup
Programmed using State Logic, Basic, C:
IEC 61131-3 programming standard
Siemens S7-mEC embedded controller

## Slide 46: PLC Programming
Programs stored in non-volatile memory, battery backup
Programmed using IEC 61131-3 programming standard
Languages: graphical (e.g., Ladder diagram) and textual (e.g., Structured Text, Sequential Function Charts)
Ref: http://www.rtaautomation.com/iec61131-3/
http://www.dogwoodvalleypress.com/uploads/excerpts/03192005214421.pdf

## Slide 47: PLC Ladder Logic Diagram
Rung 1
Rung 2
Rung 3
Timer, counter, sequencer etc.

## Slide 48: PLC Ladder Logic Example
Pilot light PL2 is to be ON when selector switch SS2 is closed, push-button PB4 is closed and limit switch LS3 is open.
Series connection
PL2=SS2 (AND) PB4 (AND) LS3

## Slide 49: PLC Scan
PLC program is scanned continuously while reading the state of physical inputs and setting the state of the physical outputs.
Scan time for one cycle is between 0-200ms.
Larger scan times might miss transient events.

## Slide 50: HMI
Human Machine Interface
Operator panel to display and control of system/device state
Programming software: Example: WinCC from Siemens

## Slide 51: SDR
Software Defined Radio
Radio communication system that has the traditional hardware components implemented in software. These include mixers, filters, amplifiers, modulator/demodulator, etc.

## Slide 52: Network Security in CPS: Siemens Approach
Use the notion of “cell protection.”
Divide plant network into “automation cells.” Inside such a cell all devices are able to communicate with each other.
Access is controlled at the entrance to each cell using a hardware device
Communication with the outside world is via VPN-protected channel.

## Slide 53: CPS Survivability
How can a CPS continue to function above a given threshold in the presence of attacks?
Despite these techniques, systems continue to be compromised.

## Slide 54: Two stories: North Pole Toys Stuxnet

## Slide 55: North Pole Toys: Basics
On-line retailer.
Carries specialized toys generally not found elsewhere.
Process: Toy Assembly, Toy Packaging and Toy Shipping
2011: Replaced the old manufacturing system with new automated industrial control system.
Files are carried on USB sticks from main server to the workshop; air gap established

## Slide 56: North Pole Toys: Attack
Day before Thanksgiving 2011…….
Instead of one toy per box, multiple toys were being placed.
Some empty boxes were being wrapped.
Initial suspicion: Incorrect PLC code; but the code found to be correct.
Discovery: kAndyKAn3 worm had infected the PLC and the main office computers.

## Slide 57: Stuxnet

## Slide 58: Uranium and its isotopes
Uranium: Naturally occurring radioactive element
Uranium 238: 99.2739 - 99.2752%
Uranium 235: 0.7198 - 0.7202%
Uranium 234: 0.0050 - 0.0059%

## Slide 59: Uranium 235
Only isotope found in nature in any appreciable quantities; is fissile, i.e., can be broken apart by thermal neutrons.

## Slide 60: Uranium enrichment: Basis
http://www.world-nuclear.org/info/inf28.html
Exploit mass difference (238 versus 235)
Produce UF6

## Slide 61: Uranium enrichment: Zippe Centrifuge
geoinfo.nmt.edu/resources/uranium/enrichment.html
Use centrifuges (rapidly revolving cylinders); pulsating magnetic field applied to the rotor; bottom is heated; rotation in vacuum
Heavier U238 atoms down and outward
Lighter U235 atoms move towards center and are collected
Banks of centrifuges used to get the desired amount of U325.
http://en.wikipedia.org/wiki/Zippe-type_centrifuge

## Slide 62: Iranian nuclear enrichment plant
Intl Atomic Energy Commission found over 1000-2000 removed from cascades in a few months!!
What happened?
About 8700 centrifuges installed; replacement rate of 10% per year (approximately 800/yr);

## Slide 63: Malware suspicion
It was found that the virus was using a zero-day vulnerability to spread.
June 17, 2010: A computer belonging to an Iranian a customer of VirusBlokAda was caught in a reboot loop.

## Slide 64: Stuxnet Spread: .LNK file via USB
Microsoft informed; the virus named Stuxnet using the file names found in the virus (.stub and MrxNet.sys)
The .LNK file drops a new copy of Stuxnet onto other systems
It also drops a rootkit which is used to hide the Stuxnet routines.
Some driver files used a certificate stolen from a company in Taiwan.

## Slide 65: Stuxnet Spread: Vulnerabilities exploited
Print spooler
Windows keyboard file
Task Scheduler file
Static password (Cyber) coded by Siemens into Step 7 software

## Slide 66: Stuxnet..cut short a long story
Designed to target Simatic WinCC Step7 software from Siemens.
A malicious DLL file intercepted commands from Step 7 to PLC that controlled frequency converters; replaced them by their own commands; the screen showed only valid commands.
Stuxnet searched for a specific value—2C CB 00 01, 9500H, 7050; codes used in Profibus communication standard.
The two 1-word codes were of frequency converters made in Finland and Iran.

## Slide 67: Stuxnet..finally
The STL code sent 47F and 1 (command to start the frequency converter and set value to 1 ).
Stuxnet strategy:
Stay quiet for 2-weeks; increase the frequency of the converters to 1,410Hz for 15 minutes; restore them to a normal frequency of 1,064Hz for for 27 days; drop the frequency down to 2Hz for 50 minutes.
Repeat above.

## Slide 68: Control Systems: Basics
Secure control: towards survivable cyber physical systems, Amin et al.,

## Slide 69: Linear feedback system
x: state vector
A: state matrix
B: Input matrix
C: Output matrix
D: Feedforward matrix
u: Control input
Y: System output
xk+1=Axk+wk
yk=Cxk+vk
w: state noise and
v: measurement noise vectors
Problem: How to ensure optimal state estimation under noisy measurements?
Gaussian random noise, zero mean and Q and R, both >0 as covariance

## Slide 70: Linear feedback system: discrete version
xk+1=Axk+wk
yk=Cxk+vk
w: state noise and
v: measurement noise vectors
Problem: How to ensure optimal state estimation under noisy measurements?
Gaussian random noise, zero mean and Q and R, both >0 as covariance.
Assumption: (A;C) is detectable and (A;Q) is stabilizable,
the estimation error covariance of the Kalman filter converges to a unique steady state value from any initial condition.

## Slide 71: Linear feedback system: robustness
xk+1=Axk+wk
yk=Cxk+vk
w: state noise and
v: measurement noise vectors
Every raw measurement of y might not arrive at the controller (estimator), e.g., due to network congestion.
Hence Kalman filters are needed that take into account packet losses (history of packet losses).
Do we know the characteristic of packet losses when under attack (QoS parameters)?
Perhaps consider state of the communications network as a stochastic event and develop new filtering techniques.

## Slide 72: Fault tolerant control (FTC)
Goal: Maintain stability and acceptable behavior in the presence of component faults by applying physical and/or analytical redundancies.
Passive FTC: Consider a fixed set of fault configurations and design the system to detect and compensate for these. Example: Control in the presence of sensor malfunction.
Active FTC: Estimate state and fault parameters using measurements and control data and reconfigure the system using different control law.

## Slide 73: PID Controller
P: Proportional
I: Integral:
D: Derivative
e: Error
u: Control input
Y: System output
Proportionality constants control the rise time, overshoot, settling time, and the steady state error of system output Y.

## Slide 74: Proportional Controller
Always a steady state error.
Error decreases with increasing gain.
Tendency to oscillate increases with increasing gain.

## Slide 75: PID Controller
Steady state error vanishes.
Tendency to oscillate increases with increasing KD=1/Ti, i.e., decreasing Ti.
Tendency to oscillate increases with increasing gain.

## Slide 76: PID Controller
KP and KI selected for oscillatory system.
Damping increases with increasing Td (KD=1/Td).
Derivative term is ineffective when Td is larger than about 1/6th of the period .

## Slide 77: Attacks on Implantable Medical Devices
Halperin et al, 2008 IEEE SS&P, pp129 -142

## Slide 78: CPS: Medical Device Attack
Implanted device
Parameter/algorithm
update computer
Pumps can be hijacked by hacking radio signals.
Then the device could be switched off
Dangerous dose of medicine could be delivered
Security alerts could be disabled
175kHz

## Slide 79: CPS: Medical Device Attack Procedure
Capture RF transmission [175kHz].
Oscilloscope allowed identification of transmissions from ICD to ICD Programmer.
RF traces analyzed using Matlab and GNU Radio toolchain to obtain symbols and bits.
This led to the discovery of the ICD –programmer communications protocol.
Reverse engineer the transmissions:

## Slide 80: CPS: Medical Device Attack Procedure
Built an eavesdropper using GNU radio library.
Establish transaction timeline.
Decoding not needed; meaning of transactions were deciphered by observing the order in which the programmer acquired the information from the ICD.
Eavesdropping with a software radio:

## Slide 81: CPS: Medical Device Attacks
Halperin et al, 2008 IEEE SS&P, pp129 -142
ICD-Programmer Communications:

## Slide 82: CPS: Medical Device: Attacks
Halperin et al, 2008 IEEE SS&P, pp129 -142
Using Universal Software Radio Peripheral and BasicTX board, several attacks were possible.
Replay attack: ICT set to a known state, replay the desired transmission and then evaluate the ICD state. .
Air gap of a few centimeters..

## Slide 83: CPS: Medical Device: Attacks
Halperin et al, 2008 IEEE SS&P, pp129 -142
Triggering ICD identification: Auto-identification trace was replayed leading to identical responses from the ICD.
Disclosing patient data: Auto-identification followed by interrogation command makes the ICD respond with patient name, diagnosis, and other details.

## Slide 84: CPS: Medical Device: Attacks
Halperin et al, 2008 IEEE SS&P, pp129 -142
Disclosing cardiac data: Replaying the start of the interrogation command sequence causes the ICD to transmit cardiac data.
Changing therapies: Therapies could be turned off by replaying captures where the programmer turns off the therapies. Once done, the ICD does not respond to dangerous cardiac conditions.

## Slide 85: Securing Medical Devices: Encryption?
Halperin et al, 2008 IEEE SS&P, pp129 -142
Should the communications between the programmer and the ICD be encrypted?

## Slide 86: Securing Medical Devices: Zero power approaches
Halperin et al, 2008 IEEE SS&P, pp129 -142
Zero-power notification: Alert patient when security-sensitive event occurs; do so by harvesting induced RF to wirelessly power a piezo-element [built on WISP: Wireless Identification Sensing Platform]
Zero-power authentication: Harvest RF energy to power cryptographically strong protocol to authenticate requests from the programmer. [Challenge-response protocol]
Sensible key-exchange: Combine ZPN and ZPA for vibration-based key distribution.

## Slide 87: CPS: Medical Device: Protocol
Halperin et al, 2008 IEEE SS&P, pp129 -142
KM: master key (Programmer)
I: IMD serial number
K=f(KM, I); IMD key
f: pseudorandom function
RC5: Block cipher
GPIO: General Purpose IO port
Nonce: Fixed in this implementation

## Slide 88: CPS: Medical Device: Protocol
Halperin et al, 2008 IEEE SS&P, pp129 -142
Programmer
WISP
Authenticate
I(dentity) and N(once)
Compute
f(KM,I)
R=RC5(K, N)
1
4
3
2
5
R’=RC5(K, N)
IMD
(R’==R)=>
GPIO high
6

## Slide 89: CPS: Medical Device: Key management
Halperin et al, 2008 IEEE SS&P, pp129 -142
Open problem for implantable devices

## Slide 90: CPS: Medical Device Attack: Results
Halperin et al, 2008 IEEE SS&P, pp129 -142

## Slide 91: Deception Attacks on Irrigation Systems
On Cyber Security for Networked Control Systems, Amin, Saurabh, Ph.D., UNIVERSITY OF CALIFORNIA, BERKELEY, 2011, 198 pages; 3473864

## Slide 92: The Gignac irrigation canal

## Slide 93: SCADA in irrigation: Physical attacks
Solar panels stolen affecting radio communications
Damaged monitoring bridge that hosts gate controllers
Installing additional pumps

## Slide 94: SCADA in irrigation: Other incidents
Tehama colusa canal, Willows, CA, USA
Maroochy water breach, near Brisbane, Australia
Harrisburg water filtering plant, Harrisburg, PA, USA

## Slide 95: SCADA in irrigation
SCADA
level
velocity
Hydraulic
structures
policies
Control
Signals (radio)
Motorized gates and
controllers

## Slide 96: Irrigation canal model
m: Number of canal pools
T, X: Cross section width and length of each pool (m)
V: Average cross-sectional velocity (m/s)
Y: Water depth
P: Offtake; lateral outflow (m2/s)
Ui-1, Ui: Opening of upstream and downstream gates
Gates

## Slide 97: Irrigation canal: Shallow Water Eqns
g: gravity (m/s2)
Sf : friction slope
Sb : bed slope (m/m)

## Slide 98: Irrigation canal: Control actions
Ui-1 and Ui: can be changed by controlling the actuators: Y: Known upstream and downstream
Yi(0, t) and Yi(X,t): known measurements
Upstream and downstream discharge:

## Slide 99: Irrigation canal: Boundary conditions
Upstream and downstream discharge:
Intermediate gates discharge:

## Slide 100: Irrigation canal: Feedback actions
Change in gate openings ui(t)
Boundary control actions are decentralized and local to each canal pool; computed using local water level measurements.

## Slide 101: Irrigation canal: Water withdrawal attack
Ji: Number of offtakes from pool i
Lateral flow along the length of the ith pool:
Indicator for jth offtake in ith canal:
Total lateral withdrawal from ith canal:

## Slide 102: Irrigation canal: Water withdrawal attack
Adversary can affect withdrawal from one or more of the Ji offtakes in canal i.
Water is withdrawn by discretely opening and closing the offtake gates.
Thus, the offtake withdrawal vector switches between different modes Q={1, 2,….N}.

## Slide 103: Irrigation canal: sensor deception attack
Adversary can affect sensor readings for upstream Yi(0, t) and Yi(X,t) and gate opening Ui(t)
This leads to a transformed water level and gate openings.

## Slide 104: Irrigation canal: Experiments

## Slide 105: Irrigation canal: Experiments

## Slide 106: CPS Design Principles

## Slide 107: Aspects to consider
Adversary models: Restrict the scope; but overly restrictive assumptions will likely limit their aplicability e.g., in DoS attacks.
Trust models: Trust in human users and devices, e.g., sensors and actuators
“Under attack” behavior: Detection and graceful degradation.
Independence in component design: Redundant authentication mechanisms that are indepenent of each other

## Slide 108: Potential research directions and educational needs

## Slide 109: CPS Gaps?
Study the overall design of selected critical CPS infrastructures and determine security gaps and their impact on functionality and safety of Singapore population.

## Slide 110: CPS Modeling: Network models
What is the state space of reach node (a subsystem)?
What are the constraints across node-states?
If and how could an attacker violate the constraints?

## Slide 111: CPS [Supply chain] Monitoring
Are the existing intrusion detection tools adequate for monitoring attacks across a supply chain?
How could nodes in a supply chain-- with Singapore as a node-- be compromised?
What monitoring tools are need to check the “health” of a supply chain given the possibility of an network attack?

## Slide 112: CPS Attack scenarios
How to defend against any such attacks?
Are there attacks different from the existing ones that could sabotage a supply chain or any CPS?

## Slide 113: CPS Control Robustness
How to design controllers that could continue to function in the presence of deception and denial of service attacks?

## Slide 114: CPS Access Control
Are RBAC and TRBAC models for access control adequate for large distributed CPS and global supply chains?

## Slide 115: CPS: Theoretical Foundations
Control theoretic [e.g., work at Berkeley]
Game theoretic [e.g., work at UT Arlington]
Verification and testing techniques[e.g., work at Purdue]
Specification-based [e.g., work at UIUC]

## Slide 116: CPS: Educational needs
Traditional IT security:
Cryptography, networks, OS, and other CS subjects
CPS security:
Interdisciplinary education needed;
Background in controls, game theory, industrial automation;
Domain background
Most importantly:
Ability to acquire the necessary background through self learning

## Slide 117: Summary
What is a CPS?
What research directions Singapore ought to consider to ensure the functionality of its CPS and consequently the safety of its people?
Why existing techniques for the detection and prevention of information-related attacks might be inadequate in CPS?

## Slide 118: References [Sample]
Secure Control: Towards Survivable Cyber-Physical Systems. Alvaro A. Ca ́rdenas Saurabh Amin Shankar Sastry, The 28th International Conference on Distributed Computing Systems Workshop, IEEE 2008.
Common Cybersecurity Vulnerabilities in Industrial Control Systems. US Department of Homeland Security. May 2011.
Cyber-Physical Systems Security for Smart Grid. White Paper. Manimaran Govindarasu, Adam Hann, and Peter Sauer. February 2012.
Improving the Security and Privacy of Implantable Medical Devices, William H. Maisel and Tadayoshi Kohno, New England Journal of Medicine 362(13):1164-1166, April 2010.
Guide to Industrial Control Systems (ICS) Security. Keith Stouffer, Joe Falco, and Karen Scarfone. NIST. 800-02. June 2011.