## Slide 1: Lecture 24 Wireless Network Security
modified from slides of Lawrie Brown
Notes: Wireless networks and communication links have become pervasive for both
personal and organizational communications. A wide variety of technologies and
network types have been adopted, including Wi-Fi, Bluetooth, WiMAX, ZigBee,
and cellular technologies. Although the security threats and countermeasures
discussed throughout this book apply to wireless networks and communications
links, there are some unique aspects to the wireless environment. We begin this
chapter with an overview of such wireless security concerns.
Then, as a case study, we look at one of the most important wireless network
security schemes: the IEEE 802.11i standard for wireless LAN security. This
standard is part of IEEE 802.11, also referred to as Wi-Fi. We begin the discussion
with an overview of IEEE 802.11, and then we look in some detail at IEEE 802.11i.

## Slide 2: Wireless, Mobile, and Bluetooth
To understand data-oriented wireless and mobile networks and security systems:
  Data-oriented wireless networks
    Wireless LAN (WLAN, 802.11)
    World Interoperability for Microwave Access (WiMAX, 802.16)
    Bluetooth (IEEE 802.15)
  Security in WLAN
    Wired Equivalent Privacy (WEP)
    Wi-Fi Protected Access (WPA, WPA 2 – IEEE 802.11i)

## Slide 3: Wireless and Mobile Networks
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers (5-to-1)!
# wireless Internet-connected devices equals # wireline Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 4: Seems Inescapable by the Internet
Wireless nodes will soon dominate the Internet.
Currently ~1B nodes, including wireline.
Urgent response to the exploding wireless demand is a necessity.
http://www.cisco.com/c/en/us/solutions/collateral/service-provider/visual-networking-index-vni/white_paper_c11-520862.html

## Slide 5: Wireless Capacity – NOW!
Scary trends in mobile wireless demand**
  Global mobile subscribers will reach 5.1 bn by 2023.
  Mobile Device units grows to 13.1 bn by 2023.
“More than 80% is landing on WiFi”, http://Wefi.com
Opportunistic wireless networking is well accepted by the users!
**Cisco (2020). Cisco Annual Internet Report (2018–2023) White Paper. Retrieved May 22, 2021 from https://www.cisco.com/c/en/us/solutions/collateral/executive-perspectives/annual-internet-report/white-paper-c11-741490.html

## Slide 6: Cellular is Full
“Sorry, America: Your wireless airwaves are full”, CNN, Feb 21, 2012.

## Slide 7: Elements of a wireless network
network
infrastructure

## Slide 8: Elements of a wireless network
wireless hosts
laptop, smartphone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility
network
infrastructure

## Slide 9: Elements of a wireless network
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points
network
infrastructure

## Slide 10: Elements of a wireless network
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access control (MAC) protocol coordinates link access
various data rates, transmission distance
network
infrastructure

## Slide 13: Elements of a wireless network
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network
network
infrastructure

## Slide 14: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 15: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
wireless nodes:
MANET, VANET

## Slide 16: Wireless Security Overview
concerns for wireless security are like those found in a wired environment
security requirements are the same:
  confidentiality, integrity, availability, authenticity,
  most significant source of risk is the underlying communications medium
Notes: The concerns for wireless security, in terms of threats, and countermeasures, are
similar to those found in a wired environment, such as an Ethernet LAN or a wired
wide-area network. The security requirements are the same in both environments:
confidentiality, integrity, availability, authenticity, and accountability. However,
some of the security threats are exacerbated in a wireless environment and some are
unique to the wireless environment. The most significant source of risk in wireless
networks is the underlying communications medium. In addition, there have
traditionally been security risks in wireless protocols that have only been addressed
in relatively recent generations of these protocols.

## Slide 17: Wireless Security
Key factors contributing to higher security risk of wireless networks compared to wired networks include:
  Channel
    Wireless networking typically involves broadcast communications, which is far more susceptible to eavesdropping and jamming than wired networks
    Wireless networks are also more vulnerable to active attacks that exploit vulnerabilities in communications protocols
  Mobility
    Wireless devices are far more portable and mobile, thus resulting in several risks
  Resources
    Some wireless devices, such as smartphones and tablets, have sophisticated operating systems but limited memory and processing resources with which to counter threats, including denial of service and malware
  Accessibility
    Some wireless devices, such as sensors and robots, may be left unattended in remote and/or hostile locations, thus greatly increasing their vulnerability to physical attacks
Notes: Wireless networks, and the wireless devices that use them, introduce a host of security
problems over and above those found in wired networks. Some of the key factors
contributing to the higher security risk of wireless networks compared to wired
networks include the following [MA10]:
• Channel: Wireless networking typically involves broadcast communications,
which is far more susceptible to eavesdropping and jamming than wired networks.
Wireless networks are also more vulnerable to active attacks that
exploit vulnerabilities in communications protocols.
• Mobility: Wireless devices are, in principal and usually in practice, far more
portable and mobile than wired devices. This mobility results in a number of
risks, described subsequently.
• Resources: Some wireless devices, such as smartphones and tablets, have
sophisticated operating systems but limited memory and processing resources
with which to counter threats, including denial of service and malware.
• Accessibility: Some wireless devices, such as sensors and robots, may be left
unattended in remote and/or hostile locations. This greatly increases their vulnerability
to physical attacks.

## Slide 18: Wireless Networking Components
Notes: In simple terms, the wireless environment consists of three components that
provide point of attack ( Figure 24.1 ). The wireless client can be a cell phone, a
Wi-Fi enabled laptop or tablet, a wireless sensor, a Bluetooth device, and so on.
The wireless access point provides a connection to the network or service. Examples
of access points are cell towers, Wi-Fi hot spots, and wireless access points to wired
local or wide-area networks. The transmission medium, which carries the radio
waves for data transfer, is also a source of vulnerability.

## Slide 19: Wireless Network Threats
accidental association
malicious association
ad hoc networks
nontraditional networks
identity theft (MAC spoofing)
man-in-the middle attacks
denial of service (DoS)
network injection
Notes: [CHOI08] lists the following security threats to wireless networks:
• Accidental association: Company wireless LANs or wireless access points to
wired LANs in close proximity (e.g., in the same or neighboring buildings) may
create overlapping transmission ranges. A user intending to connect to one
LAN may unintentionally lock on to a wireless access point from a neighboring
network. Although the security breach is accidental, it nevertheless exposes
resources of one LAN to the accidental user.
• Malicious association: In this situation, a wireless device is configured to
appear to be a legitimate access point, enabling the operator to steal passwords
from legitimate users and then penetrate a wired network through a legitimate
wireless access point.
• Ad hoc networks: These are peer-to-peer networks between wireless
computers with no access point between them. Such networks can pose a
security threat due to a lack of a central point of control.
• Nontraditional networks: Nontraditional networks and links, such as personal
network Bluetooth devices, barcode readers, and handheld PDAs pose a
security risk both in terms of eavesdropping and spoofing.
• Identity theft (MAC spoofing): This occurs when an attacker is able to
eavesdrop on network traffic and identify the MAC address of a computer
with network privileges.
• Man-in-the middle attacks: This type of attack is described in Chapter 21 in
the context of the Diffie-Hellman key exchange protocol. In a broader sense,
this attack involves persuading a user and an access point to believe that they
are talking to each other when in fact the communication is going through an
intermediate attacking device. Wireless networks are particularly vulnerable
to such attacks.
• Denial of service (DoS): This type of attack was discussed in detail in
Chapter 7 . In the context of a wireless network, a DoS attack occurs when an
attacker continually bombards a wireless access point or some other accessible
wireless port with various protocol messages designed to consume
system resources. The wireless environment lends itself to this type of attack,
because it is so easy for the attacker to direct multiple wireless messages at
the target.
• Network injection: A network injection attack targets wireless access points
that are exposed to non-filtered network traffic, such as routing protocol
messages or network management messages. An example of such an attack is
one in which bogus reconfiguration commands are used to affect routers and
switches to degrade network performance.

## Slide 20: Securing Wireless Transmissions
principal threats are eavesdropping, altering or inserting messages, and disruption
countermeasures for eavesdropping:
  signal-hiding techniques
  encryption
the use of encryption and authentication protocols is the standard method of countering attempts to alter or insert transmissions
Notes: Following [CHOI08], we can group wireless security measures into those dealing
with wireless transmissions, wireless access points, and wireless networks (consisting
of wireless routers and endpoints).
The principal threats to wireless transmission
are eavesdropping, altering or inserting messages, and disruption. To deal with
eavesdropping, two types of countermeasures are appropriate:
• Signal-hiding techniques: Organizations can take a number of measures to
make it more difficult for an attacker to locate their wireless access points,
including turning off service set identifier (SSID) broadcasting by wireless
access points; assigning cryptic names to SSIDs; reducing signal strength to the
lowest level that still provides requisite coverage; and locating wireless access
points in the interior of the building, away from windows and exterior walls.
Greater security can be achieved by the use of directional antennas and of
signal-shielding techniques.
• Encryption: Encryption of all wireless transmission is effective against
eavesdropping to the extent that the encryption keys are secured.
The use of encryption and authentication protocols is the standard method of
countering attempts to alter or insert transmissions.
The methods discussed in Chapter 7 for dealing with denial of service apply
to wireless transmissions. Organizations can also reduce the risk of unintentional
DoS attacks. Site surveys can detect the existence of other devices using the same
frequency range, to help determine where to locate wireless access points. Signal
strengths can be adjusted and shielding used in an attempt to isolate a wireless
environment from competing nearby transmissions.

## Slide 21: Securing Wireless Networks
the main threat involving wireless access points is unauthorized access to the network
principal approach for preventing such access is the IEEE 802.1X standard for port-based network access control
  provides an authentication mechanism for devices wishing to attach to a LAN or wireless network
use of 802.1X can prevent rogue access points and other unauthorized devices from becoming insecure backdoors
Notes: The main threat involving wireless access
points is unauthorized access to the network. The principal approach for preventing
such access is the IEEE 802.1X standard for port-based network access control. The
standard provides an authentication mechanism for devices wishing to attach to a
LAN or wireless network. The use of 802.1X can prevent rogue access points and
other unauthorized devices from becoming insecure backdoors.

## Slide 22: Wireless Security Techniques
use encryption
use anti-virus and anti-spyware software and a firewall
turn off identifier broadcasting
change the identifier on your router from the default
change your router’s pre-set password for administration
allow only specific computers to access your wireless network
Notes: [CHOI08] recommends the following techniques
for wireless network security:
1. Use encryption. Wireless routers are typically equipped with built-in
encryption mechanisms for router-to-router traffic.
2. Use anti-virus and anti-spyware software, and a firewall. These facilities
should be enabled on all wireless network endpoints.
3. Turn off identifier broadcasting. Wireless routers are typically configured to
broadcast an identifying signal so that any device within range can learn of
the router’s existence. If a network is configured so that authorized devices
know the identity of routers, this capability can be disabled, so as to thwart
attackers.
4. Change the identifier on your router from the default. Again, this measure
thwarts attackers who will attempt to gain access to a wireless network using
default router identifiers.
5. Change your router’s pre-set password for administration. This is another
prudent step.
6. Allow only specific computers to access your wireless network. A router
can be configured to only communicate with approved MAC addresses.
Of course, MAC addresses can be spoofed, so this is just one element of a
security strategy.

## Slide 23: Mobile Device Security
An organization’s networks must accommodate:
  Growing use of new devices
    Significant growth in employee’s use of mobile devices
  Cloud-based applications
    Applications no longer run solely on physical servers in corporate data centers
  De-perimeterization
    There are a multitude of network perimeters around devices, applications, users, and data
  External business requirements
    The enterprise must also provide guests, third-party contractors, and business partners network access using various devices from a multitude of locations
Notes: Prior to the widespread use of smartphones, the dominant paradigm for computer
and network security in organizations was as follows. Corporate IT was tightly controlled.
User devices were typically limited to Windows PCs. Business applications
were controlled by IT and either run locally on endpoints or on physical servers
in data centers. Network security was based upon clearly defined perimeters that
separated trusted internal networks from the untrusted Internet. Today, there have
been massive changes in each of these assumptions. An organization’s networks
must accommodate the following:
• Growing use of new devices: Organizations are experiencing significant growth
in employee’s use of mobile devices. In many cases, employees are allowed to
use a combination of endpoint devices as part of their day-to-day activities.
• Cloud-based applications: Applications no longer run solely on physical
servers in corporate data centers. Quite the opposite, applications can run
anywhere—on traditional physical servers, on mobile virtual servers, or in the
cloud. Additionally, end users can now take advantage of a wide variety of
cloud-based applications and IT services for personal and professional use.
Facebook can be used for an employee’s personal profile or as a component
of a corporate marketing campaign. Employees depend upon Skype to speak
with friends abroad or for legitimate business video conferencing. Dropbox
and Box can be used to distribute documents between corporate and personal
devices for mobility and user productivity.
• De-perimeterization: Given new device proliferation, application mobility,
and cloud-based consumer and corporate services, the notion of a static network
perimeter is all but gone. Now there are a multitude of network perimeters
around devices, applications, users, and data. These perimeters have also
become quite dynamic as they must adapt to various environmental conditions
such as user role, device type, server virtualization mobility, network location,
and time-of-day.
• External business requirements: The enterprise must also provide guests,
third-party contractors, and business partners network access using various
devices from a multitude of locations.
The central element in all of these changes is the mobile computing device.
Mobile devices have become an essential element for organizations as part of the
overall network infrastructure. Mobile devices such as smartphones, tablets, and
memory sticks provide increased convenience for individuals as well as the potential
for increased productivity in the workplace. Because of their widespread use and
unique characteristics, security for mobile devices is a pressing and complex issue.
In essence, an organization needs to implement a security policy through a combination
of security features built into the mobile devices and additional security controls
provided by network components that regulate the use of the mobile devices.

## Slide 24: Security Threats
Lack of physical security controls
Use of untrusted networks
Use of untrusted mobile devices
Use of applications created by unknown parties
Interaction with other systems
Use of untrusted content
Use of location services
Notes: If a mobile device is used on premises, it can
connect to organization resources over the organization’s own in-house wireless
networks. However, for off-premises use, the user will typically access organizational
resources via Wi-Fi or cellular access to the Internet and from the Internet to the
organization. Thus, traffic that includes an off-premises segment is potentially
susceptible to eavesdropping or man-in-the-middle types of attacks. Thus, the
security policy must be based on the assumption that the networks between the
mobile device and the organization are not trustworthy.
Use of Applications Created by Unknown Parties By design, it is easy to find
and install third-party applications on mobile devices. This poses the obvious risk of
installing malicious software. An organization has several options for dealing with
this threat, as described subsequently.
Interaction with other Systems A common feature found on smartphones
and tablets is the ability to automatically synchronize data, apps, contacts, photos,
and so on with other computing devices and with cloud-based storage. Unless an
organization has control of all the devices involved in synchronization, there is
considerable risk of the organization’s data being stored in an unsecured location,
plus the risk of the introduction of malware.
Use of Untrusted Content Mobile devices may access and use content that other
computing devices do not encounter. An example is the Quick Response (QR) code,
which is a two-dimensional barcode. QR codes are designed to be captured by a mobile
device camera and used by the mobile device. The QR code translates to a URL, so
that a malicious QR code could direct the mobile device to malicious Web sites.
Use of Location Services The GPS capability on mobile devices can be used
to maintain a knowledge of the physical location of the device. While this feature
might be useful to an organization as part of a presence service, it creates security
risks. An attacker can use the location information to determine where the device
and user are located, which may be of use to the attacker.
Mobile Device Security Strategy
With the threats listed in the preceding discussion in mind, we outline the principal
elements of a mobile device security strategy. They fall into three categories: device
security, client/server traffic security, and barrier security (Figure 24.2).
Device Security A number of organizations will supply mobile devices for
employee use and pre-configure those devices to conform to the enterprise security
policy. However, many organizations will find it convenient or even necessary to
adopt a bring-your-own-device (BYOD) policy that allows the personal mobile
devices of employees to have access to corporate resources. IT managers should be
able to inspect each device before allowing network access. IT will want to establish
configuration guidelines for operating systems and applications.

## Slide 25
Notes: With the threats listed in the preceding discussion in mind, we outline the principal
elements of a mobile device security strategy. They fall into three categories: device
security, client/server traffic security, and barrier security (Figure 24.2).

## Slide 26: Wireless Fidelity (Wi-Fi) Alliance
802.11b
  first 802.11 standard to gain broad industry acceptance
Wireless Ethernet Compatibility Alliance
  industry consortium formed in 1999 to address the concern of products from different vendors successfully interoperating
  later renamed the Wi-Fi Alliance
Notes: The first 802.11 standard to gain broad industry acceptance was 802.11b. Although
802.11b products are all based on the same standard, there is always a concern
whether products from different vendors will successfully interoperate. To meet
this concern, the Wireless Ethernet Compatibility Alliance (WECA), an industry
consortium, was formed in 1999. This organization, subsequently renamed the
Wi-Fi (Wireless Fidelity) Alliance, created a test suite to certify interoperability
for 802.11b products. The term used for certified 802.11b products is Wi-Fi . Wi-Fi
certification has been extended to 802.11g products. The Wi-Fi Alliance has also
developed a certification process for 802.11a products, called Wi-Fi5 . The Wi-Fi
Alliance is concerned with a range of market areas for WLANs, including enterprise,
home, and hot spots.
More recently, the Wi-Fi Alliance has developed certification procedures for
IEEE 802.11 security standards, referred to as Wi-Fi Protected Access (WPA). The
most recent version of WPA, known as WPA2, incorporates all of the features of
the IEEE 802.11i WLAN security specification.

## Slide 27: Wireless Fidelity (Wi-Fi) Alliance
term used for certified 802.11b products is Wi-Fi
  has been extended to 802.11g products
Wi-Fi Protected Access (WPA)
  Wi-Fi Alliance certification procedures for IEEE 802.11 security standards
  WPA2 incorporates all of the features of the IEEE 802.11i WLAN security specification
Notes: The first 802.11 standard to gain broad industry acceptance was 802.11b. Although
802.11b products are all based on the same standard, there is always a concern
whether products from different vendors will successfully interoperate. To meet
this concern, the Wireless Ethernet Compatibility Alliance (WECA), an industry
consortium, was formed in 1999. This organization, subsequently renamed the
Wi-Fi (Wireless Fidelity) Alliance, created a test suite to certify interoperability
for 802.11b products. The term used for certified 802.11b products is Wi-Fi . Wi-Fi
certification has been extended to 802.11g products. The Wi-Fi Alliance has also
developed a certification process for 802.11a products, called Wi-Fi5 . The Wi-Fi
Alliance is concerned with a range of market areas for WLANs, including enterprise,
home, and hot spots.
More recently, the Wi-Fi Alliance has developed certification procedures for
IEEE 802.11 security standards, referred to as Wi-Fi Protected Access (WPA). The
most recent version of WPA, known as WPA2, incorporates all of the features of
the IEEE 802.11i WLAN security specification.

## Slide 28: Wireless LAN Security
Wired Equivalent Privacy (WEP) algorithm
  802.11 privacy
Wi-Fi Protected Access (WPA)
  set of security mechanisms that eliminates most 802.11 security issues
  based on the current state of the 802.11i standard
Wi-Fi Alliance certifies vendors in compliance with the full 802.11i specification under WPA2
WPA3 - upcoming
Robust Security Network (RSN)
  final form of the 802.11i standard
Notes: There are two characteristics of a wired LAN that are not inherent in a wireless
LAN.
1. In order to transmit over a wired LAN, a station must be physically connected
to the LAN. On the other hand, with a wireless LAN, any station within radio
range of the other devices on the LAN can transmit. In a sense, there is a
form of authentication with a wired LAN in that it requires some positive and
presumably observable action to connect a station to a wired LAN.
2. Similarly, in order to receive a transmission from a station that is part of a
wired LAN, the receiving station also must be attached to the wired LAN.
On the other hand, with a wireless LAN, any station within radio range can
receive. Thus, a wired LAN provides a degree of privacy, limiting reception of
data to stations connected to the LAN.
These differences between wired and wireless LANs suggest the increased
need for robust security services and mechanisms for wireless LANs. The
original 802.11 specification included a set of security features for privacy and
authentication that were quite weak. For privacy, 802.11 defined the Wired
Equivalent Privacy (WEP) algorithm. The privacy portion of the 802.11
standard contained major weaknesses. Subsequent to the development of WEP,
the 802.11i task group has developed a set of capabilities to address the WLAN
security issues. In order to accelerate the introduction of strong security into
WLANs, the Wi-Fi Alliance promulgated Wi-Fi Protected Access (WPA) as a
Wi-Fi standard. WPA is a set of security mechanisms that eliminates most 802.11
security issues and was based on the current state of the 802.11i standard. The
final form of the 802.11i standard is referred to as Robust Security Network
(RSN) . The Wi-Fi Alliance certifies vendors in compliance with the full 802.11i
specification under the WPA2 program.

## Slide 29: Data Integrity in 802.11
To detect data modification
How?
  Calculating ICV (Integrity Check Value) over the received data
  Comparing it with the ICV attached in the message
ICV : CRC-32 (Cyclic Redundancy Check 32 bits)
  Not cryptographically computed -> Weak.

## Slide 30: Data Integrity in 802.11
802.11 header is not protected by ICV  redirection attack;
Replay attack;

## Slide 31: WEP Confidentiality Issues
First, the IV size at 24 bits was too short – key space is only 16,777,216;
Second, WEP did not specify how to select an IV for each packet;
Third, WEP did not even make it mandatory to vary the IV on a per-packet basis — this means WEP explicitly allowed reuse of per-packet keys.
Fourth, there was no mechanism to ensure that the IV was unique on a per station basis -- thus making a collision even more likely.
No support for STA to authenticate the network.
Finally, simply concatenating the IV with the pre-shared key to obtain a per-packet key is cryptographically unsecure, making WEP vulnerable to attacks.

## Slide 32: WEP vs WAP vs WPA2

## Slide 33: WEP vs WAP vs WPA2

## Slide 34: WPA3 - WPA3 (Wi-Fi Protected Access 3)
  Latest generation in mainstream security for wireless networks.
  Improves the level of security compared to the widely popular WPA2 standard (released in 2004) yet maintains backward compatibility.
https://www.mist.com/wpa3-just-the-essentials-on-the-latest-in-wi-fi-security/

## Slide 35: WPA3 – Main Forms
  WPA3 Personal (WPA-3 SAE) Mode
    static passphrase-based method. It provides
    Simultaneous Authentication of Equals (SAE),
  WPA3 Enterprise Mode (WPA3 ENT):
    requires management frame protection.
    An optional, stronger 192bit consistent cryptographic suite is also provided for those who are more security conscious.
  Wi-Fi Enhanced Open Mode
    increases privacy in open networks
    prevents passive eavesdropping by encrypting traffic even when a password is not used
    anyone can still connect to the network.

## Slide 36: WPA3 – Key Features
Management Frame Protection (MFP):
  Unicast management frames are encrypted, preventing, for example, illegitimate de-authorization of clients (for operating man-in-the-middle attack, or for IDS/IPS systems to kick clients out.
  This means WIDS/WIPS systems now have less brute-force ways to enforce clients’ policies and will rely more heavily on notifying the system admin about rogue/honeypot APs, for example.
Simultaneous Authentication of Equals (SAE):
  SAE provides a more secure, password-based authentication and key agreement mechanism even when passwords are not following complexity requirements.
  It protects from brute-force attacks and makes unwanted decrypting of sessions (during or after the session) a lot harder – just knowing the passphrase isn’t enough to decrypt the session.
Transition mode:
  This means falling back to WPA2 for connecting clients that don’t support WPA3.

## Slide 37: 802.11i RSN security services
Authentication: between a user and an Authentication Server that provides mutual authentication and generates temporary keys to be used between the client and the AP over the wireless link
Access control: enforces the use of the authentication function, routes the messages properly, and facilitates key exchange
  It can work with a variety of authentication protocols
Privacy with message integrity: MAC-level data are encrypted along with a message integrity code that ensures that the data have not been altered
Notes: The 802.11i RSN security specification defines the following services.
• Authentication: A protocol is used to define an exchange between a user and an
AS (authentication server) that provides mutual authentication and generates
temporary keys to be used between the client and the AP over the wireless link.
• Access control: This function enforces the use of the authentication function,
routes the messages properly, and facilitates key exchange. It can work with a
variety of authentication protocols.
• Privacy with message integrity: MAC-level data (e.g., an LLC PDU) are
encrypted along with a message integrity code that ensures that the data have
not been altered.

## Slide 38: Summary
  IEEE 802.11i wireless LAN security
    IEEE 802.11i services
    IEEE 802.11i phases of operation
    Discovery phase
    Authentication phase
    Key management phase
    Protected data transfer phase
    The IEEE 802.11i pseudorandom function
Wireless Security
  Wireless network threats
  Wireless security measures
Mobile device security
  Security threats
  Mobile device security strategy
IEEE 802.11 wireless LAN overview
  The Wi-Fi alliance
  IEEE 802 protocol
  IEEE 802.11 network components and architectural model
  IEEE 802.11 services