## Slide 1: IT 6533 Health Information Security and Privacy
Physical Security

## Slide 2: Physical Security
Physical security addresses design, implementation, and maintenance of countermeasures that protect physical resources of an organization.
Most controls can be circumvented if an attacker gains physical access.
Physical security is as important as logical security.
Notes: Introduction
Physical security addresses design, implementation, and maintenance of countermeasures that protect the physical resources of an organization.
Most of the technology-based controls discussed to this point can be circumvented, if an attacker gains physical access to the devices being controlled.
Some computer systems are constructed in such a way that it easy to steal the hard drive and the information it contains.
As a result, physical security should receive as much attention as logical security in the security development life cycle.

## Slide 3: Major Sources of Physical Loss
People (!)
Extreme temperature (heat, cold)
Gases
Liquids
Living organisms
Projectiles
Movement
Energy anomalies (surge of power)
From Donn B. Parker
Notes: Seven Major Sources of Physical Loss
From Donn B. Parker
Extreme temperature: heat, cold
Gases: war gases, commercial vapors, humid or dry air, suspended particles
Liquids: water, chemicals
Living organisms: viruses, bacteria, people, animals, insects
Projectiles: tangible objects in motion, powered objects
Movement: collapse, shearing, shaking, vibration, liquefaction, flows waves, separation, slide
Energy anomalies: electrical surge or failure, magnetism, static electricity, aging circuitry; radiation: sound, light, radio, microwave, electromagnetic, atomic.

## Slide 4: Physical Security Threats
We can group these threats:
Environmental threats (including natural disasters)
Technical threats
Human-caused threats, both malicious and accidental.
Notes: In this section, we first look at the types of physical situations and occurrences that can constitute a threat to information systems. There are a number of ways in which such threats can be categorized. What is important is to be able to understand the spectrum of threats to information systems, so that responsible administrators can be assured that prevention measures are comprehensive. We organized the threats into the following categories:
• Environmental threats
• Technical threats
• Human-caused threats
We begin with a discussion of natural disasters, which are a prime, but not the only, source of environmental threats. Then we look specifically at environmental threats, followed by technical and human-caused threats.

## Slide 5: Forces of Nature
Wind (tornado, hurricane)
  Location
  Construction
Flood
  Location
Electrical storms
  Power redundancy
  Construction
  Location
Ice storm, blizzard
  Location
  Construction
Earthquake
  Location
  Construction
Extremes of heat and cold
  Location
  HVAC

## Slide 6: Environmental Threats
Inappropriate temperature and humidity
Fire and smoke
Water
Chemical, radiological, biological hazards
Dust (especially paper dust)
Infestation (mold, insects, vermin)
Notes: This category encompasses conditions in the environment that can damage or interrupt the service of information systems and the data they house. Off-site, there may be severe region-wide damage to the public infrastructure and, in the case of severe hurricanes, it may take days, weeks, or even years to recover from the event.
Inappropriate Temperature and Humidity - computers and related equipment are designed to operate within a certain temperature range, typically 10 - 32 deg Celsius (50 - 90 deg F). Outside this range, they might continue to operate but produce undesirable results. High humidity also threatens electrical and electronic equipment.
Fire and Smoke is a threat to human life and property both from direct flame and also from heat, release of toxic fumes, water damage from fire suppression, and smoke damage. Electrical fires can acrid smoke that may damage equipment and may be poisonous or carcinogenic. The most common fire threat is from fires that originate within a facility, but a more uncontrollable threat is faced from wildfires/bushfires.
Water Damage liquids in proximity to computer equipment pose an obvious threat. The primary danger is an electrical short. A pipe may burst from a fault, or freezing. Sprinkler systems are a major threat if incorrectly set off. Less common, but more catastrophic, is floodwater that leaves a muddy residue that is difficult to clean up.
Chemical, radiological, and biological hazards pose a growing threat, both from intentional attack and from accidental discharge. None should be present, but either accidental or intentional intrusion is possible.Their primary risk is to personnel.
Dust is a prevalent concern that is often overlooked.
Infestation covers a broad range including mold,insects,and rodents.

## Slide 7: Technical Threats
Electric power is essential to run equipment
  power utility problems:
    under-voltage - dips/brownouts/outages, interrupt service
    over-voltage - surges/faults/lightening, can destroy chips
    noise - on power lines, may interfere with device operation
Electromagnetic interference (EMI)
  from line noise, motors, fans, heavy equipment, other computers, nearby radio stations and microwave relays
  can cause intermittent problems with computers
Notes: Technical threats encompass electrical power and electromagnetic emissio threats.
Electrical power is essential to the operation of an information system. All of the electrical and electronic devices in the system require power, and most require uninterrupted utility power. Power utility problems can be broadly grouped into three categories:
under-voltage - when equipment receives less voltage than required for normal operation, from temporary dips in voltage supply, brown-outs to power outages. Generally, no damage is done, but service is interrupted.
over-voltage - is more serious, from a utility company supply anomaly, internal wiring fault, or by lightening. A sufficient surge can destroy silicon-based components, including processors and memories.
noise - on power-lines, which can endure through the filtering circuitry of the power supply and interfere with signals inside electronic devices, causing logical errors.
Electromagnetic Interference (EMI), from noise along a power supply line, motors, fans, heavy equipment, and even other computers generate electrical noise that can cause intermittent problems with the computer you are using. This noise can be transmitted through space as well as nearby power lines. Also from high-intensity emissions from nearby commercial radio stations and microwave relay antennas. Even low-intensity devices, such as cellular telephones, can interfere with sensitive electronic equipment.

## Slide 8: Human-Caused Threats
Less predictable, may be targeted, harder to deal with
Include:
  unauthorized physical access leading to other threats
  theft of equipment / data
  vandalism of equipment / data
  misuse of resources
Notes: Human-caused threats are more difficult to deal with than the environmental and technical threats so far discussed. Human-caused threats are less predictable than other types of physical threats. Worse, human-caused threats are specifically designed to overcome prevention measures and/or seek the most vulnerable point of attack. We can group such threats into the following categories:
• Unauthorized physical access: Those who are not employees should not be in the building or building complex at all unless accompanied by an authorized individual. Not counting PCs and workstations, information system assets, such as servers, mainframe computers, network equipment, and storage networks, are generally housed in restricted areas. Access to such areas is usually restricted to only a certain number of employees. Unauthorized physical access can lead to other threats, such as theft, vandalism, or misuse.
• Theft: This threat includes theft of equipment and theft of data by copying. Eavesdropping and wiretapping also fall into this category. Theft can be at the hands of an outsider who has gained unauthorized access or by an insider.
• Vandalism: This includes destruction of equipment and destruction of data.
• Misuse: This category includes improper use of resources by those who are authorized to use them, as well as use of resources by individuals not authorized to use the resources at all.

## Slide 9: Mitigation Measures for Environmental Threats
Inappropriate temperature and humidity
  environmental control equipment, power
Fire and smoke
  alarms, preventive measures, fire mitigation
  smoke detectors, no-smoking policy, housekeeping
Water
  manage lines, equipment location, cutoff sensors
Other threats
  appropriate technical counter-measures, limit dust entry, pest control
Notes: In this section, we look at a range of technique for preventing, or in some cases simply deterring, physical attacks.
Dealing with Inappropriate Temperature and Humidity is primarily a matter of having environmental-control equipment of appropriate capacity and appropriate sensors to warn of thresholds being exceeded. Beyond that, the principal requirement is the maintenance of a power supply.
Dealing with fire involves a combination of alarms, preventive measures (such as the list given in the text), and fire mitigation. To deal with the smoke threat, needs smoke detectors in every room with computer equipment, under raised floors, and over suspended ceilings. Smoking should not be permitted in computer rooms.
Prevention and mitigation measures for water threats must encompass their range. For plumbing leaks measures can be taken to sensibly locate equipment, and shutoff valves should be clearly visible. To deal with both plumbing leaks and other sources of water, sensors are vital, located on the floor of computer rooms, as well as under raised floors, and enabled to automatically cut off power in the event of a flood.
For chemical, biological, and radiological threats, specific technical approaches are available including infrastructure design, sensor design and placement, mitigation procedures, personnel training, and so forth. Standards and techniques in these areas continue to evolve. For dust hazards, the obvious prevention method is to limit dust, through the use and proper maintenance of filters and regular IS room maintenance. For infestations, regular pest control procedures may be needed, starting with maintaining a clean environment.

## Slide 10: Mitigation Measures Technical Threats
Electric power for critical equipment use
  Uninterruptible power supply (UPS)
  Emergency power generator
Electromagnetic interference (EMI)
  Filters and shielding
  Dedicated circuits
Notes: To deal with brief power interruptions, an uninterruptible power supply (UPS) should be employed for each piece of critical equipment. The UPS is a battery backup unit that can maintain power to processors, monitors, and other equipment for a period of minutes. UPS units can also function as surge protectors, power noise filters, and automatic shutdown devices when the battery runs low.
For longer blackouts or brownouts, critical equipment should be connected to an emergency power source, delivered by a generator. For reliable service, a range of issues need to be addressed by management, including product selection, generator placement, personnel training, testing and maintenance schedules, and so forth.
To deal with electromagnetic interference, a combination of filters and shielding can be used. The specific technical details will depend on the infrastructure design and the anticipated sources and nature of the interference.

## Slide 11: Mitigation Measures Human-Caused Threats
Physical access control
  IT equipment, wiring, power, communications, media
Several areas to consider
  restrict building access, locked area, secured, power switch secured, tracking devices for portable equipment
Intruder sensors / alarms
Notes: The general approach to human-caused physical threats is physical access control. Physical access control should cover not just IT hardware, but also locations of wiring, electrical power, HVAC equipment and distribution system, telephone and communications lines, backup media, and documents. We can suggest a spectrum of approaches that can be used to restrict access to equipment. These methods include:
1. Physical contact with a resource is restricted by restricting access to the building in which it is housed. This approach is intended to deny access to outsiders, but does not address the issue of unauthorized insiders or employees. Techniques include controlled areas patrolled or guarded by personnel, barriers that isolate each area, entry points in the barrier (doors), and locks or screening measures at each entry point.
2. Physical contact with a resource is restricted by putting it in a locked cabinet, safe, or room. Same techniques as for 1.
3. A machine may be accessed, but be secured (e.g. bolted) to a fixed object. This will deter theft, but not vandalism, unauthorized access, or misuse.
4. A security device controls the power switch.
5. A movable resource may have a tracking device so that a sensor can alert security personnel or trigger a barrier to prevent removal.
6. A portable object is equipped with a tracking device so that its current position can be monitored continually.
Effective physical access control may also includes a variety of sensors and alarms to detect intruders and unauthorized access or movement of equipment.

## Slide 12: Management Roles
General management: responsible for facility security
IT management and professionals: responsible for environmental and access security
Information security management and professionals: perform risk assessments and implementation reviews; implement technical controls.
Notes: Community Roles
General management: responsible for the security of the facility in which the organization is housed and the policies and standards for secure operation.
IT management and professionals: responsible for environmental and access security in technology equipment locations and for the policies and standards of secure equipment operation.
Information security management and professionals: perform risk assessments and implementation reviews for the physical security controls implemented by the other two groups.

## Slide 13: Physical Access Controls
Secure facility: a physical location engineered with controls designed to minimize risk from physical threats
A secure facility can take advantage of natural terrain, traffic flow, and degree of urban development; can complement these with protection mechanisms (fences, gates, walls, guards, alarms)
Notes: Facilities Management
Before examining access controls, understand the concept of a secure facility and its design.
From the point of view of facilities management, a secure facility is a physical location that has been engineered with controls designed to minimize the risk of attacks from physical threats.
A secure facility can use the natural terrain; traffic flow, urban development, and can complement these features with protection mechanisms, such as fences, gates, walls, guards, and alarms.

## Slide 14: Computer Rooms, Wiring Closets
Require special attention to ensure confidentiality, integrity, and availability of information
Logical controls are easily defeated if attacker gains physical access to computing equipment
Custodial staff often the least scrutinized persons who have access to offices; are given greatest degree of unsupervised access
Notes: Computer Rooms and Wiring Closets
Computer rooms and wiring and communications closets are facilities that require special attention to ensure the confidentiality, integrity, and availability of information.
Logical access controls are easily defeated, if an attacker gains physical access to the computing equipment.
Custodial staff are often the least scrutinized of employees and non-employees who have access to offices. Yet custodians are given the greatest degree of unsupervised access.

## Slide 15: Protecting the Secure Facility
Physical Barriers
  Exterior walls, fencing, and gates
  Locks and keys
  Interior walls
Identification
  ID Cards and badges
Monitoring
  Electronic monitoring
  Alarm systems
Human Barriers
  Guards
  Other staff
Notes: Controls for Protecting the Secure Facility
There are a number of physical security controls and issues that the organization’s communities of interest should consider together when implementing physical security:
Walls, Fencing, and Gates.
Guards to apply human reasoning.
Dogs to provide their keen sense of smell and hearing and to be placed in harm’s way in lieu of humans.
ID Cards and Badges
Locks and Keys
Mantraps
Electronic Monitoring
Alarms and Alarm Systems
Computer Rooms
Walls and Doors

## Slide 16: ID Cards and Badges
Common in health care; can be color-coded by area.
Ties physical security with information access control
  ID card is typically concealed
  Name badge is visible
Serve as simple form of biometrics (facial recognition)
Should not be only means of control as cards can be easily duplicated, stolen, and modified
Notes: ID Cards and Badges
One area of access control that ties physical security with information access control is the use of identification cards (ID) and name badges. An ID card is typically worn concealed, whereas a name badge is visible.
These devices are forms of biometrics (facial recognition) to identify and authenticate an authorized individual with access to the facility.
With the addition of a magnetic strip or radio chip, the ID card can provide access control.
A name badge or ID should not be the only control for access to restricted areas, as they can be easily duplicated, stolen, and modified.
Tailgating occurs when an authorized individual presents a key and a door is opened, but other individuals, who may or may not be authorized, also enter the unlocked door.

## Slide 17: Locks and Keys
Two types of locks: mechanical and electromechanical
Locks can also be divided into four categories: manual, programmable, electronic, biometric
Locks can fail; alternative procedures for controlling access must be put in place
Locks fail in one of two ways
  Fail-safe (open) lock
  Fail-secure lock
Fail-secure locks may violate fire codes
Notes: Locks and Keys
There are two types of locks: mechanical and electro-mechanical.
The mechanical lock relies on a key of carefully shaped pieces of metal that turn tumblers to release secured loops of steel, aluminum, or brass (in brass padlocks).
The electro-mechanical lock can accept a variety of inputs including keys that are magnetic strips on ID Cards, radio signals from name badges, PINs typed into a keypad.
Locks are divided into four categories: manual, programmable, electronic, and biometric.
As part of general management’s responsibility for the physical environment, the management of keys and locks is a fundamental concern.
Sometimes locks fail and facilities need alternative procedures for access.
Locks fail in one of two ways: when the lock of a door fails and the door becomes unlocked, that is a fail-safe lock; when the lock of a door fails and the door remains locked, this is a fail-secure lock.

## Slide 18: Electronic Monitoring
Records events where other types of physical controls are impractical or incomplete
May use cameras with video recorders; includes closed-circuit television (CCT) systems
Drawbacks
  Reactive; do not prevent access or prohibited activity
  Recordings often not monitored in real time; must be reviewed to have any value
Some monitors can call attention to changes in real time
Notes: Electronic Monitoring
Used to record events within a specific area or areas where other types of physical controls are not practical.
Monitoring frequently uses cameras viewing individuals, while on the other end of these cameras are video cassette recorders and related machinery that captures the video feed.
These systems have drawbacks as for the most part they are reactive and do not prevent access or prohibited activity.
Recorded monitoring requires an individual to review the information collected.

## Slide 19: Alarms and Alarm Systems
Alarm systems notify monitoring station when an event occurs
Detect fire, intrusion, environmental disturbance, or an interruption in services
Rely on sensors that detect event; e.g., motion detectors, smoke detectors, thermal detectors, glass breakage detectors, weight sensors, contact sensors, vibration sensors
Notes: Alarms and Alarm Systems
Alarm systems notify appropriate individuals when a predetermined event or activity occurs.
This could be a fire, a break-in or intrusion, an environmental disturbance, such as flooding, or an interruption in services, such as a loss of power.
Burglar alarm systems detect intrusions into unauthorized areas and notify either a local or remote security agency to react.
These systems rely on a number of sensors that detect the intrusion: motion detectors, thermal detectors, glass breakage detectors, weight sensors, and contact sensors.

## Slide 20: Interior Walls and Doors
Information asset security sometimes compromised by construction of facility walls and doors
Facility walls typically either standard interior wall or fire-rated wall
High-security areas must have firewall-grade or masonry walls to provide physical security from potential intruders and improve resistance to fires
Doors allowing access to high security rooms should be evaluated
Recommended that push or crash bars be installed on computer rooms and closets
Notes: Interior Walls and Doors
The security of information assets can sometimes be compromised because of the construction of the walls and doors of the facility.
The walls in a facility are typically: standard interior or firewall.
All high-security areas, such as computer rooms and wiring closets, must have firewall grade walls surrounding them.
This provides not only physical security from potential intruders but from fires as well.
The doors that allow access into these types of secured rooms should also be evaluated.
Computer rooms and wiring closets can have push or crash bars can be installed.
Such devices meet building codes, but provide much higher levels of security than the standard door pull handle.

## Slide 21: Fire Security and Safety
A very serious threat to safety of patients and people who work in an organization is possibility of fire.
Fires account for more property damage, personal injury, and death than many other threats.
Imperative that physical security plans examine and implement strong measures to detect and respond to fires.

## Slide 22: Fire Detection and Response
Fire suppression systems: devices installed and maintained to detect and respond to a fire
Deny an environment of heat, fuel, or oxygen
  Water and water mist systems
  Carbon dioxide systems
  Soda acid systems
  Gas-based systems
Notes: Fire Detection and Response
Fire suppression systems are devices installed and maintained to detect and respond to a fire, potential fire, or combustion situation.
These devices typically work to deny an environment of one of the three requirements for a fire to burn: temperature, fuel, and oxygen.
Water and water mist systems reduce the temperature of the flame to extinguish it and to saturate some categories of fuels to prevent ignition.
Carbon dioxide systems rob fire of its oxygen.
Soda acid systems deny fire its fuel, preventing spreading.
Gas-based systems disrupt the fire’s chemical reaction but leave enough oxygen for people to survive for a short time.

## Slide 23: Fire Detection
Fire detection systems fall into two general categories: manual and automatic
Part of a complete fire safety program includes individuals who monitor chaos of fire evacuation to prevent an attacker accessing offices
There are three basic types of fire detection systems: thermal detection, smoke detection, flame detection
Notes: Fire Detection
Before a fire can be suppressed, it must be detected.
Fire detection systems fall into two general categories: manual and automatic.
Manual fire detection systems include human responses, such as calling the fire department, as well as manually activated alarms, such as sprinklers and gaseous systems.
During the chaos of a fire evacuation, an attacker can easily slip into offices and obtain sensitive information. As part of a complete fire safety program, it is advisable to designate individuals as floor monitors.
There are three basic types of fire detection systems: thermal detection, smoke detection, and flame detection.
The thermal detection systems contain a sophisticated heat sensor that operates in one of two ways, fixed temperature, and rate-of-rise.
Smoke-detection systems are perhaps the most common means of detecting a potentially dangerous fire, and are required by building codes:
Smoke detectors operate in one of three ways:
1) photoelectric sensors project and detect an infrared beam, if interrupted activates alarm or suppression systems.
2) ionization sensors contains a small amount of a harmless radioactive material within a detection chamber. When certain by-products of combustion enter, a change in the level of electrical conductivity activates the detector.
3) air-aspirating detectors take in air, filtering it, and moving it through a chamber containing a laser beam. If the laser beam is diverted or refracted by smoke particles, the system is activated.
The flame detector is a sensor that detects the infrared or ultraviolet light produced by an open flame.
These systems require direct line-of-sight with the flame and compare the flame “signature” to a database to determine whether or not to activate the alarm and suppression systems.
While highly sensitive, flame detection systems are expensive and must be installed where they can scan all areas of the protected area.

## Slide 24: Fire Suppression
Systems consist of portable, manual, or automatic apparatus
Portable extinguishers are rated by the type of fire: Class A, Class B, Class C, Class D
Installed systems apply suppressive agents; usually either sprinkler or gas systems
Notes: Fire Suppression
Fire suppression systems can consist of portable, manual, or automatic apparatus. Portable extinguishers are rated by the type of fire:
Class A: fires of ordinary combustible fuels. Use water and multi-purpose, dry chemical fire extinguishers.
Class B: fires fueled by combustible liquids or gases, such as solvents, gasoline, paint, lacquer, and oil. Use carbon dioxide, multi-purpose dry chemical and halon fire extinguishers.
Class C: fires with energized electrical equipment or appliances. Use carbon dioxide, multi-purpose, dry chemical and halon fire extinguishers.
Class D: fires fueled by combustible metals, such as magnesium, lithium, and sodium. Use special extinguishing agents and techniques.
Manual and automatic fire response can include installed systems designed to apply suppressive agents. These are usually either sprinkler or gaseous systems.
All sprinkler systems are designed to apply liquid, usually water, to all areas in which a fire has been detected.
In sprinkler systems, the organization can implement wet pipe, dry pipe, or pre-action systems.
Water mist sprinklers are the newest form of sprinkler systems and rely on micro-fine mists instead of traditional shower-type systems.

## Slide 25: Gas Emission Systems
Until recently, two types of systems: carbon dioxide and Halon
Carbon dioxide robs a fire of oxygen supply (but is dangerous as h … well, it’s dangerous because it can silently kill people!)
Halon is clean but has been classified as ozone-depleting substance; new installations are prohibited
Alternative “clean” agents include FM-200, Inergen, FE-13 (trifluromethane)
Notes: Gaseous Emission Systems
Chemical gas systems can be used in the suppression of fires.
Until recently there were only two major types of gaseous systems: carbon dioxide and halon.
Carbon dioxide robs a fire of its oxygen supply.
Halon is a clean agent, which means that it does not leave any residue when dry, nor does it interfere with the operation of electrical or electronic equipment. Unfortunately the EPA has classified halon as an ozone-depleting substance, and therefore new installations are prohibited.
Alternative clean agents include the following:
FM-200
Inergen
Carbon dioxide
FE-13 (trifluromethane)

## Slide 26: Failure Of Supporting Utilities
Supporting utilities (heating, ventilation and air conditioning; power; water; and others) have significant impact on continued safe operation of a facility
Each utility must be properly managed to prevent potential damage to information and information systems
Notes: Failure Of Supporting Utilities And Structural Collapse
Supporting utilities, such as heating, ventilation and air conditioning, power, water, and other utilities, have a significant impact on the continued safe operation of a facility.
Extreme temperatures and humidity levels, electrical fluctuations and the interruption of water, sewage, and garbage services can create conditions that inject vulnerabilities in systems designed to protect information.

## Slide 27: Specifying HVAC
Multiple smaller units
N+1 redundancy, at least
Size for extreme ambient temperatures (both low and high)
Consider the increasing density of equipment
In cold climates, consider “economizing” systems
Don’t forget emergency power for the HVAC

## Slide 28: Water Problems
Lack of water poses problem to systems, including functionality of fire suppression systems and ability of water chillers to provide air conditioning
Surplus of water, or water pressure, poses a real threat (flooding; leaks); location of computer rooms
  No pipes (except sprinklers) within computer rooms
  Under-floor water detection
Very important to integrate water detection systems into alarm systems that regulate overall facilities operations
Notes: Water Problems
Lack of water poses problem to systems, including the functionality of fire suppression systems, and the ability of water chillers to provide air-conditioning.
On the other hand, a surplus of water, or water pressure, poses a real threat.
It is therefore important to integrate water detection systems into the alarm systems that regulate overall facilities operations.

## Slide 29: Power Management
Electrical quantity (voltage level; amperage rating) is a concern, as is quality of power (cleanliness; proper installation)
Noise that interferes with the normal 60 Hertz cycle can result in inaccurate time clocks or unreliable internal clocks inside CPU
Overloading a circuit causes problems with circuit tripping and can overload electric conductors, increasing risk of fire if breakers are not properly sized.
Notes: Power Management and Conditioning
Not only is electrical quantity (voltage level and amperage rating) of concern, but so is the quality of the power (cleanliness and proper installation).
Interference with the normal pattern of the electrical current is referred to as noise in the current.
Any noise that interferes with the normal 60 Hertz cycle can result in inaccurate time clocks or, even worse, unreliable internal clocks inside the CPU.
Grounding
  Grounding ensures that the returning flow of current is properly discharged to the ground.
  If this is not properly installed, anyone touching a computer or other electrical device could be used as a ground source, causing damage to equipment and injury or death to the person.
  Power should also be provided in sufficient amperage to support needed operations.
  Overloading a circuit not only causes problems with the circuit tripping but can also overload the power load on an electrical cable, creating the risk of fire.

## Slide 30: Grounding
“Neutral” conductor: carries the return current of a circuit. Bonded to the center tap of a transformer.
  If this is not properly installed, anyone touching a computer or other electrical device could be used as a ground source, causing damage to equipment and injury or death to the person.
Safety ground: often also bonded to the center tap of the transformer; should be connected to earth ground.
Signal ground or reference ground: a reference for low-voltage signals.
Notes: Power Management and Conditioning
Not only is electrical quantity (voltage level and amperage rating) of concern, but so is the quality of the power (cleanliness and proper installation).
Interference with the normal pattern of the electrical current is referred to as noise in the current.
Any noise that interferes with the normal 60 Hertz cycle can result in inaccurate time clocks or, even worse, unreliable internal clocks inside the CPU.
Grounding
  Grounding ensures that the returning flow of current is properly discharged to the ground.
  If this is not properly installed, anyone touching a computer or other electrical device could be used as a ground source, causing damage to equipment and injury or death to the person.
  Power should also be provided in sufficient amperage to support needed operations.
  Overloading a circuit not only causes problems with the circuit tripping but can also overload the power load on an electrical cable, creating the risk of fire.

## Slide 31: Purpose of Safety Ground
American Power Conversion
Notes: Circuit breaker trips if there’s a “short” between power and case

## Slide 32: Dedicated Circuits
Purpose: to isolate computer equipment from other loads
Other loads can trip circuit breakers!
Some loads (large motors, fluorescent lights) generate electrical noise

## Slide 33: Determining Power Requirements
Watts: power consumed; heat dissipated
Volt-amps: apparent power; voltage times current.
W = PF * VA
  For power-factor-corrected power supplies, W=VA (PF = 1)
  For “small” equipment, PF is about 0.60, and W will be less than VA.
UPSs have both a maximum Watt rating and a maximum VA rating

## Slide 34: Determining Power Requirements
HVAC
Lighting
“Convenience” power
These may be interrupted briefly.

## Slide 35: Uninterruptible Power Supply (UPS)
In case of power outage, UPS is backup power source for major computer systems
Four basic UPS configurations:
  Standby (battery backup)
  Line-interactive
  True online (double conversion online)
  Rotating (motor-generators)
Notes: Uninterruptible Power Supplies (UPSs)
In case of power outage, a UPS is a backup power source for major computer systems.
There are four basic configurations of UPS:
  the standby
  line-interactive
  the true online
  rotating
A standby or offline UPS is an off-line battery backup that detects the interruption of power to the power equipment
A ferroresonant standby UPS is still an offline UPS - the ferroresonant transformer reduces power problems.
The line-interactive UPS is always connected to the output, so has a much faster response time and incorporates power conditioning and line filtering
The true online UPS works in the opposite fashion to a standby UPS since the primary power source is the battery, with the power feed from the utility constantly recharging the batteries - this model allows constant feed to the system, while completely eliminating power quality problems

## Slide 36: UPS Sizes
To 1,000 VA: Desktop equipment
1 to 2.5 kVA: Servers, wiring closets, etc
2.5 to 10 kVA: Small computer rooms
10 to 100 kVA: Data centers
100 + kVA: Large installations

## Slide 37: Designing UPS Systems
Transfer Switch
Utility Power
Generator
Transfer Switch
Non-Critical Load
Critical Load
UPS
Maintenance Bypass

## Slide 38: Dual-Corded Systems
Power Supply
Power Supply
For most effective use, the power to each power supply should be independent, i.e. two UPSs on different circuits.
One Socket?

## Slide 39: Emergency Shutoff
An important aspect of power management is the need to be able to stop power immediately should current represent a risk to human or machine safety
Most computer rooms and wiring closets equipped with an emergency power shutoff
Accident-resistant cover is essential
Notes: Emergency Shutoff
One important aspect of power management in any environment is the need to be able to stop power immediately should the current represent a risk to human or machine safety.
Most computer rooms and wiring closets are equipped with an emergency power shutoff, which is usually a large red button, prominently placed to facilitate access, with an accident-proof cover to prevent unintentional use.

## Slide 40: Maintenance of Facility Systems
Physical security must be documented and constantly evaluated and tested
Documentation of facility’s configuration, operation, and function should be integrated into disaster recovery plans and operating procedures
Testing helps improve the facility’s physical security and identify weak points
Notes: Testing Facility Systems
Just as with any phase of the security process, the physical security of the facility must be constantly documented, evaluated, and tested.
Documentation of the facilities configuration, operation, and function is integrated into disaster recovery plans and standing operating procedures.
Testing provides information necessary to improve the physical security in the facility and identifies areas weak points.

## Slide 41: Inventory Management
Computing equipment should be inventoried and inspected on a regular basis
Classified information should also be inventoried and managed
Physical security of computing equipment, data storage media and classified documents varies for each organization
Notes: Inventory Management
As with other organizational resources, computing equipment should be inventoried and inspected on a regular basis. Similarly classified information should also be inventoried and managed.
Whenever a classified document us reproduced, a stamp should be placed on the original before it is copied.
This stamp states the document’s classification level and document number for tracking.
Each classified copy is issued to its receiver, who signs for the document.