## Slide 1
Viscoelasticity

## Slide 2
Made from petroleum and coal
Forms of pitch are called tar, bitumen, or asphalt
Is a visco-elastic material and behaves as both a solid (elastic) and a liquid (viscosity)
Behaves like a solid at room temperature, is shattered with a hard impact
Behaves like a fluid and will flow over time, but extremely slowly
Solid at short timescales
Liquid at long timescales
Everyday Materials That Exhibit
Solid and Liquid Behaviors
Pitch-black/Resin
Silly Putty
What happens when you bounce silly putty- is it a solid or liquid?
Solid
What happens when you roll it into a ball and lay it on the table for 5 minutes?
Liquid if you have patience
What happens when you slightly pull on the putty?
Kinda solid (it coils back when you remove stress, is elastic)
What happens when you pull on it a lot?
Liquid (permanent deformation, it flows)
Notes: Pitch (resin) - Wikipedia

## Slide 3
Longest running lab experiment, Guinness Book of Records
In 1927 Professor Parnell (University of Queensland, Australia) heated a sample of pitch (resin) and poured it into a glass funnel with a sealed stem
He allowed the pitch to cool and settle for three years, and then in 1930 he cut the funnel's stem
Pitch started to and has been flowing since 1930
Experiment demonstrates the fluidity and high viscosity of pitch
The Tenth Watch for the tenth Pitch Drop.
Pitch Drop Experiment
Notes: Pitch (resin) - Wikipedia

## Slide 4
Viscoelasticity
  Property of materials that exhibit both viscous and elastic characteristics when undergoing deformation
Viscous materials
  Resist shear flow and deform in shape when a stress is applied
  viscosity is the result of the diffusion (movement) of atoms or molecules
Elastic materials
  Strain when stretched and immediately return to their original state once the stress is removed
  elasticity is usually the result of bond stretching
Difference Between
Elasticity, Viscosity and Visco-Elasticity

## Slide 5
Stress
Strain Rate
Strain rate and stress –liquids

## Slide 6
Strain rate and stress –shear thickening

## Slide 7
Strain rate and stress –shear thinning

## Slide 8
Strain vs time for viscoelastic materials
When a constant stress (force) is applied, initially there is an elastic response
e.g. silly putty bouncing
If the stress is applied for a long time, the long time response is like a liquid
(strain increases in time)

## Slide 9
Difference Between Elasticity and Viscosity
Elasticity is the slope of stress versus strain graph
  Higher the slope higher the elasticity
  Lower the slope, lower the elasticity
Viscosity is the slope of stress versus strain rate graph
  Higher the slope higher the viscosity
  Lower the slope, lower the viscosity

## Slide 10
Categories of Materials Based on
Shear Stress-Strain Rate Behaviors
Viscosity is the slope of stress versus strain rate graph
Depending on the change of stress (y-value) versus strain rate (x-value) the materials can be categorized as
  Newtonian material
  Non-Newtonian fluid
  Plastic material

## Slide 11
Newtonian material
  Shear Stress versus Shear Rate plot is linear
  Its slope gives viscosity
  Viscosity does not change in the material
  Viscosity is positive
  Newtonian fluids are the simplest models of studying viscosity
  While no real fluid fits the definition perfectly, many common liquids and gases, such as water and air, can be assumed to be Newtonian for practical calculations under ordinary conditions
Viscosity is the slope of stress versus strain rate graph

## Slide 12
Examples of Newtonian material
The plot of shear stress versus strain rate is linear (straight line)
Note: the plot passes through origin
  It means that when strain rate is zero, the shear stress is also zero
For Newtonian materials viscosity is obtained by calculating the slope of this plot
Slope of shear stress versus strain rate plot is proportional to viscosity of Newtonian fluid
Higher the slope (steeper the line), the higher the viscosity
Lower the slope (flatter the line), the lower the viscosity
In adjacent plot, we note that water is less viscous than oil

## Slide 13
Non-Newtonian material
  Shear Stress versus Shear Rate plot is non-linear (not a straight line)
  Further categories: Pseudo-plastic fluids, Dilatant fluid
  Viscosity changes in the material and depends on the stress experienced by the material
  Viscosity can change when under force to either more liquid (decrease in viscosity) or more solid (increase in viscosity)
  Examples:
    Ketchup, becomes runnier when shaken and is thus a non-Newtonian fluid
    Many salt solutions and molten polymers commonly found in substances such as custard, honey, toothpaste, starch suspensions, corn starch, paint, blood, melted butter, and shampoo.

## Slide 14
Non-Newtonian material
  Further categories: Pseudo-plastic fluids, Dilatant fluid
  Pseudo-plastic fluids (Shear Thinning fluids)
    Viscosity decreases with increased stress in a non-linear way
    The plot of shear stress versus shear rate becomes less steep as the shear rate increases
  Dilatant fluids (Shear Thickening fluids)
    Viscosity increases with increased stress in a non-linear fashion
    The plot of shear stress versus shear rate becomes steeper as the shear rate increases

## Slide 15
Non-Newtonian material Examples
Oobleck:
  Is Corn starch suspended in water
  When stirred slowly it looks milky, when stirred vigorously it feels like a very viscous liquid
  A person may walk on a large tub of oobleck without sinking due to its shear thickening properties, as long as the individual moves quickly enough to provide enough force with each step to cause the thickening
  If a person were to punch or hit Oobleck, it would thicken and act like a solid
  After the blow, the Oobleck will go back to its thin liquid-like state
  The shear stress versus strain rate plot is not linear, it becomes steeper with increasing strain rate
  Slope of shear stress versus strain rate plot increases with strain rate

## Slide 16
Non-Newtonian material Examples
Flubber (slime):
  Made by missing white "school" glue) and borax
  Flows under low stresses but breaks under higher stresses and pressures
Ketchup
Ketchup is a shear thinning fluid
Its viscosity decreases with increasing shear stress
Its motion is initially difficult at slow rates of deformation, but will flow more freely at high rates
Shaking an inverted bottle of ketchup can cause it to transition to a lower viscosity, resulting in a sudden gush of the shear thinned ketchup
The shear stress versus strain rate plot is not linear, it becomes shallower with increasing strain rate
Slope of shear stress versus strain rate plot decreases with strain rate

## Slide 17
Fun with Non-Newtonian Fluid - Lamar University
Video link

## Slide 18
Newtonian
and
Non-Newtonian materials
Video Link

## Slide 19
Plastic material
  Shear Stress does not depend on Shear Rate
  The data between shear stress and shear (or strain) rate does not show any correlation

## Slide 20
Shear-thickening liquids: Viscosity increases with the rate of shear strain
Shear-thinning liquids: Viscosity decreases with the rate of shear strain
Thixotropic liquids: Become less viscous over time when shaken, agitated, or otherwise stressed
Dilatant liquids: Become more viscous over time when shaken, agitated, or otherwise stressed
Bingham plastics: Behave as a solid at low stresses but flow as a viscous fluid at high stresses
Summary Of Non-Newtonian Fluids

## Slide 21
Models for Studying Visco-Elasticity
Series connection of a spring and a dashpot: Maxwell model
https://www.youtube.com/watch?v=ZVK1qVkXfC4
https://www.youtube.com/watch?v=gMx78yGpej4
Solid at short timescales (High frequency)
Liquid at long timescales (low frequency)

## Slide 22
Spring and dashpot model:
Maxwell model of ViscoElasticity

## Slide 23
Spring and dashpot model:
Maxwell model of ViscoElasticity

## Slide 24
Spring and dashpot model:
Maxwell model of ViscoElasticity

## Slide 25
Kelvin-Voight Model
Parallel connection of a spring and a dashpot: Kelvin-Voight model
https://www.youtube.com/watch?v=q9emsMcG8cc

## Slide 26
After stretching and releasing a plastic bag,
  It goes back a bit (elastic recovery), however
  it does not completely go back like a rubber band(permanent strain)